## Slide 1: DIPLOMA IN FIRE & SAFETY ENGINEERING DIPLOMA IN INDUSTRIAL SAFETY (APPROVED BY BSS, GOVT. OF INDIA)
(An ISO 9001-2015 Certified Safety Training and Consulting Organization)

## Slide 2: NATIONAL SAFETY DAY – 4th MARCH NATIONAL FIRE DAY- 14th APRIL

## Slide 3: WHY SAFETY ???

## Slide 4: WHY SAFETY???
MORAL
LEGAL
FINANCIAL

## Slide 5: MORAL
Humanitarian reason, employer (owner or client) have the moral responsibility to provide
Safe Work Place
Safe Equipments / Tools
Safe Working Condition

## Slide 6: LEGAL
As per the law,
  Organization should full fill the legal requirement
  To avoid fines and penalties

## Slide 7: FINANCIAL
When an accident occurs, direct and indirect cost plays important role ……
DIRECT COST
INDIRECT COST

## Slide 8: DIRECT COST
Costs directly accumulated from the accident
Measureable Cost
Directly From The Accident
Insured Cost
Examples
  First Aid Cost
  Medical Treatment Cost
  Compensation Cost

## Slide 9: INDIRECT COST
Cannot be measured which arises indirectly as the consequence of the event
Hidden Cost
Not Usually Insurable
Examples
  Cost of overtime as a result of the accident
  Cost of selecting, employing, training, educating new employees training for new workers

## Slide 10: HSE
H - HEALTH
S - SAFETY
E - ENVIRONMENT

## Slide 11: HEALTH
Health is a state of complete physical, mental and social well being
not merely the absence of diseases or infirmity

## Slide 12: SAFETY
condition of being protected from injury

## Slide 13: ENVIRONMENT
Environment means surroundings
Surrounding in which an organization operates
Avoid pollution of Air, Water, Land
Not to effect the natural resources, flora human and their inter relationship

## Slide 14: DUTIES & RESPONSIBILITIES OF HSE OFFICER
1.Ensuring compliance with respect to health, safety, environmental as per the company, project HSE plan & statutory regulation
2. Ensuring & monitoring implementation of HSE policy & plan
3. Interacting & coordinating with client and other agencies
4. Monitoring safety procedure & their complaints
5. Ensuring and monitoring all working personal understand their HSE responsibilities

## Slide 15
Conducting and organizing HSE training program
Conducting internal safety audit, safety meeting, mock drill, emergency evacuation drill
Organizing HSE promotional activities
Reporting and recording of accident investigation
Inspect the work place to identify hazard
Making report to the findings and recommend corrective action to the site management
Periodic inspection of fire and safety equipments

## Slide 16
Preparing & updating company Safety Manual, HSE Plan, Job Safety Plan, Job Safety Analysis, Site Safety Rules, Emergency Plan
Ensure the availability and quality of PPE
Guiding and advising latest HSE norms and regulations to the management
Coordinate and maintain waste management systems
Discuss the safety issue with the management during weekly or monthly meeting

## Slide 18: FIRE
Fire is a chemical chain reaction between Fuel, Heat and oxygen

## Slide 19: CLASSIFICATION OF FIRE
 | DESCRIPTION | EXAMPLE
A (Solid) | Fire involving ordinary combustible solid materials | Wood, Paper, Textiles
B (Liquid) | Fire involving flammable liquids | Petroleum Products, Paints
C (Gases) | Fire involving gases or liquefied gases | LPG, H2S, H2
D (Metal) | Fire that occur in combustible metals | Sodium, Zinc, Potassium, Mg

## Slide 20: METHODS OF HEAT TRANSFER
CONDUCTION
Heat transfer through a medium of solid body
CONVECTION
Heat transfer through upward motion of heated matters
RADIATION
Heat transfer through air heat wave

## Slide 21: FIRE TRIANGLE

## Slide 22: EXTINGUISHING METHODS
STARVATION
Limitation or removal of fuel from the scene of fire is known as starvation
SMOTHERING or BLANKETING
Limitation or removal of oxygen from the scene of fire is known as smothering
COOLING
Limitation or removal of heat from the scene of fire is known as cooling

## Slide 23: EXTINGUISHING METHODS
STARVATION - REMOVAL OF FUEL
SMOTHERING - REMOVAL OF OXYGEN
COOLING - REMOVAL OF HEAT

## Slide 24: EXTINGUISHING MEDIA
WATER
FOAM
DCP ( DRY CHEMICAL POWDER - NaHCO₃ , NH4H2PO4)
CO2
SAND

## Slide 27: HOW TO USE FIRE EXTINGUISHER
It is easy to remember how to use a fire extinguisher, you can remember a shot form PASS which stands for
Pull
Aim
Squeeze
Sweep

## Slide 30: CLASSIFICATION OF FIRE EXTINGUISHER

## Slide 31: TYPES OF FIRE EXTINGUISHER
WATER

## Slide 32: TYPES OF FIRE EXTINGUISHER
FOAM

## Slide 33
D - DRY
C - CHEMICAL
P - POWDER
TYPES OF FIRE EXTINGUISHER

## Slide 34: FIRE EXTINGUISHEN ANATOMY

## Slide 35: FIRE EXTINGUISHEN ANATOMY
CO2 TYPE

## Slide 36: COLOUR OF EXTINGUISHER
WATER - RED
FOAM - CREAM
DCP POWDER - BLUE
CARBON DIOXIDE - BLACK

## Slide 37: TYPES OF EXTINGUISHERS
STORED PRESSURE
Stored pressure fire extinguishers are easily the most common type
In these units, the expellant (propellant) is stored in the same cylinder as the agent itself
Different agents (Water, Foam, DCP Powder) used in the fire extinguisher may require different propellants (Nitrogen, Dry Air)
Dry Chemical Extinguishers typically use Nitrogen or Dry Air as propellant
Water and Foam Extinguishers typically use Dry Air as propellant

## Slide 39: TYPES OF EXTINGUISHERS
CARTRIDGE TYPE
In cartridge operated units, the dry chemical is stored in the non-pressurized cylinder
while the propellant; either “Dry Air” or Nitrogen is stored in a separate cartridge located on the side of the unit

## Slide 41: ADVANTAGES OF DCP
Harmless to skin
Non-conductor of electricity
Good for blast fire
Better than co2 - on liquid fire
Non-toxic and non-corrosive

## Slide 42: DISADVANTAGES OF DCP
DCP cannot be used on metal fire like Na, Mg
DCP cannot be used to produce inert atmosphere to prevent gas/vapour

## Slide 43: FIRE EXTINGUISHER CHECKLIST
SI.NO | LOCATION | TYPE | PRESSER GUAGE | SAFETY PIN | DUE DATE | OUTER CYLINDER | HOSE NOZZLE | REMARK
1 | Workshop | ABC |  |  | 10/22 |  |  | Nil
2 | Office | CO2 |  |  | 10/22 |  |  | Nil

## Slide 44: DEFINITIONS
ACCIDENTS
Accident is an unplanned event that cause personal injury, property damage, equipment damage or environmental pollution
INJURY
Injury is harmful condition / damage to body as a result of an accident
HAZARD
Hazard is a potential to cause harm to the body

## Slide 45: DEFINITIONS
RISK
Risk is the combination of Likelihood (chance) of occurrence accident and Consequence (Severity) of the accident
R = L x C
NEARMISS
Near miss is an unplanned event which does not cause any personal injury, property damage, equipment damage or environmental pollution but it has potential to cause accident. (In feature)
TOOL BOX TALK
Tool box talk is a pre-job meeting in which supervisor / safety officer will explain about the job to be done and the hazard present in that job

## Slide 46: DEFINITIONS
Who is a COMPETENT PERSON ?
One who is capable of identifying and predicting hazards in the work place
- Competent Person

## Slide 47: STANDARED SAFETY SIGNAGE
MANDATORY- BLUE & WHITE

## Slide 48
PROHIBITION – RED & BLACK
STANDARD SAFETY SIGNAGE

## Slide 49
WARNING- YELLOW & BLACK
STANDARD SAFETY SIGNAGE

## Slide 50: STANDARD SAFETY SIGNAGE
SAFE CONDITION- GREEN & WHITE

## Slide 51
FIRE EQUIPMENT
STANDARD SAFETY SIGNAGE

## Slide 52: FIRE FIGHTING EQUIPMENTS
FIRE BLANKETS
HOSE REELS
FIRE FIGHTING HOSE
FIRE MONITOR
FIRE HYDRANT
SPRINKLER SYSTEM

## Slide 53: FIRE FIGHTING EQUIPMENTS
FIRE BLANKETS

## Slide 54: FIRE FIGHTING EQUIPMENTS
HOSE REELS

## Slide 55: FIRE FIGHTING EQUIPMENTS
FIRE FIGHTING HOSE

## Slide 56: FIRE FIGHTING EQUIPMENTS
FIRE MONITOR

## Slide 57: FIRE FIGHTING EQUIPMENTS
FIRE HYDRANT

## Slide 58: FIRE FIGHTING EQUIPMENTS
SPRINKLER SYSTEM

## Slide 59: FIRE DETECTORS
SMOKE DETECTOR

## Slide 60: FIRE DETECTORS
HEAT DETECTORS – Temperature Sensor

## Slide 61: COMMON CAUSES OF FIRE
Spark from electricity
Smoking
Hot Work
Naked Flame
Hot Surface
Spark from Vehicles
Static Electricity
Lightning

## Slide 62: CONSEQUENCE OF FIRE
People get Injured & Killed
Damage to equipment/Building
Environment Damage

## Slide 63: PERSONAL PROTECTIVE EQUIPMENT
(PPE)

## Slide 64
Hierarchy of Risk Control

## Slide 65: PPES

## Slide 66: PERSONAL PROTECTIVE EQUIPMENT
PPE is equipment that will protect the user against health or safety risks at work

## Slide 67: TYPES OF PPES
Respiratory Protective Equipment
e.g. SCBA, Air Respirators etc.
Non- Respiratory Protective Equipment
e.g. Hard Hat, Gloves, Goggles, Safety Shoes etc.

## Slide 68: NON-RESPIRATORY PROTECTIVE EQUIPMENTS
COMMON PPE
Head Protection
Eye & Face Protection
Hand Protection
Foot Protection

## Slide 69: HEAD PROTECTION
Prevention of head injures is an important factor in every job
Head Injuries are caused by falling, flying object or by jumbling the head against a fixed object

## Slide 70: HEAD PROTECTION
HEAD INJURIES

## Slide 71: EYE & FACE PROTECTION
To protect face from flying particle, splashing liquids, chemicals, chemical gas, vapours, potentially injurious light radiation suitable eye protector equipment to be given

## Slide 72: TYPES OF EYE & FACE PROTECTION
Safety Glasses
Safety Goggles
Face Shields
Welding Goggles
Laser Safety Glass

## Slide 73: EYE & FACE PROTECTION

## Slide 74: FOOT PROTECTION
To protect feet and leg from falling objects, sharp objects, hot surface and wet surface suitable feet / leg protector equipment to be used
  Safety shoes should be sturdy and acts as a protective covering to toe
  Some shoes contain metal insole to protect feet from puncture wounds

## Slide 75: FOOT PROTECTION

## Slide 76: HAND PROTECTION
Hand protection equipment must be given to protect from hands from burns, abrasion, cuts, punctures, bruise, chemical exposure

## Slide 77: HAND PROTECTION

## Slide 78: TYPES OF GLOVES
Leather Gloves
Cotton Gloves
Chemical Protection Gloves
Insulated Rubber Gloves
Welding Gloves

## Slide 79: EAR PROTECTION
Hearing protection device, also known as a HPD, is an ear protection device worn in or over the ears while exposed to hazardous noise (>85dB, 8hrs) to prevent noise-induced hearing loss
  Ear Muff
  Ear Plug

## Slide 80: HEARING PROTECTORS
Ear Plugs - Preferred ( 20-30 dB )
Ear Muffs – 2nd Choice ( 15-30 dB )
Double Hearing Protectors ( plug & muff ) used for levels over 115 dB

## Slide 81: NOISE LEVELS
Measured in decibels ( dB )
* Whisper - 10-20 dB
* Speech - 60 dB
* Noisy Office - 80 dB
* Passing Truck - 100 dB
* Jet Engine – 150 dB
Osha Limit – 85 dB

## Slide 82: PERMISSIBLE EXPOSURE LIMIT – PEL
permissible noise exposure
Duration per day ( hours ) | Sound Level ( dB )
8 HOURS | 90 dB
4 HOURS | 95 dB
2 HOURS | 100 dB
1 HOURS | 105 dB
½ HOURS | 110 dB
¼ HOURS | 115 dB

## Slide 83: RESPIRATORY PROTECTIVE EQUIPMENT
Respiratory protective equipment are life saving equipment

## Slide 84: TYPES OF PROTECTIVE DEVICES
Air Purifying Devices (APD)
Air Supplying Devices (ASD)
Combination of air purifying and air supplying devices

## Slide 85: AIR PURIFYING DEVICES
Air purifying device cleans the contaminated atmosphere
Various types of air purifying device
* Mechanical Filter Cartridge
* Chemical Cartridge
* Gas Mask
* Powered Air Purifying Devices

## Slide 86: AIR PURIFYING DEVICES

## Slide 87: AIR SUPPLYING DEVICES
Air supplying devices provide respirable atmosphere to the wearer, independent of the ambient air
Types of Air Supplying Devices
Self Contained Breathing Apparatus (SCBA)
Compressed Air Breathing Apparatus (CABA)
Emergency Escaping Breathing Apparatus (EEBA)
Air Line Respirator (ALR)

## Slide 88: BREATHING APPARATUS ANATOMY

## Slide 89: SAFETY INSPECTION
Definition
It is the process of identification of hazards
It helps to give control measure
During a Site Safety Inspection
House Keeping
Safety Sign Board
Welfare Facility
Fencing & Security
Stores & Storage System
Fire Extinguisher

## Slide 90
Fire Procedures
First Aid Facility
PPE (Personal Protective Equipment)
Barricading
Scaffolding & Working Platform
Ladder
Cranes & Lifting Equipment
Excavation
Confined Space
Electricity
Over Head & Under Ground Services
Electrical Equipment & Tools
Welding Equipment
Hazardous Substances To Health
Other Hazards

## Slide 91: HOUSE KEEPING
GLOBAL SAFETY STUDIES

## Slide 92: HOUSE KEEPING
Definition
Place for everything and everything in its proper place
Good House Keeping is the key to Safety
House Keeping
is
Everyone’s Responsibility

## Slide 93: HOUSE KEEPING
Benefits of House Keeping
Good house keeping prevents accidents and injuries
Good house keeping save space, time and materials
When a work place is clean workers feel better, think better, and do better
Good impression with visitors
Hazard elimination

## Slide 94: HOUSE KEEPING
Accidents due to poor house keeping
Tripping over loose objects on floors, stairs and platforms
Falling objects cause hit injury
Slipping on greasy, wet or dirty surface

## Slide 95: HOUSE KEEPING
INJURIES FROM SLIP FALL &TRIP FALL
Broken bones
Back or spine injury
Sprains
Death

## Slide 96: HOUSE KEEPING
GOOD HOUSE KEEPING
All material should be properly stored
Keep bolts, nuts, etc… in a tray/ bucket
Pipes, scaffold materials, etc… are potential trip hazard. Don’t store in the walkway
Don’t store materials on working platform and near access Ladder / Stair
Don’t route cables & hoses through staircase / ladder posing potential trip hazard
Don’t drain sticky material/oil on floor posing slip fall hazard

## Slide 97: HOUSE KEEPING
Don’t use fire water for cleaning
Don’t block access to fire and emergency equipment

## Slide 98: HOUSE KEEPING
Good House Keeping Checklist
Walls cleans
Window cleans
Provide proper lighting system
Platform in good condition
Stairs clean and dry
Free from oil, grease etc…
Safe and free access to work position
Employees Facilities
Waste Disposal
Storage
Tools and Equipment

## Slide 99: HOUSE KEEPING
WHAT IS YOUR FAVORITE PLACE TO WORK ?

## Slide 100: HOUSE KEEPING
BAD HOUSEKEEPING
Example: Waste container over flowing

## Slide 101: HOUSE KEEPING
GOOD HOUSE KEEPING

## Slide 102: HOUSE KEEPING
BAD HOUSE KEEPING

## Slide 103: ENVIRONMENT
GLOBAL SAFETU STUDIES

## Slide 104: ENVIRONMENT
DEFINITION
Environment means the surrounding in which as organization operate including Air, Water, Land, natural resources, flora human and their inter relationship.

## Slide 105: ENVIRONMENT
TYPES OF POLLUTION
AIR POLLUTION
WATER POLLUTION
LAND POLLUTION

## Slide 106: ENVIRONMENT
Effects of pollution
Reduced lung functioning
Irritation of Eyes, Nose, and Mouth
Asthma attack
Respiratory disease
Reduce energy level
Head ache
Mental disorder
Cancer
Death

## Slide 107: ENVIRONMENT
How to save environment
Do not waste water
Prevent pollution on the ground, air, and water by avoiding any chemical spills
Ensure all waste is collected and placed in to the specific containers
Use toilet facilities
Do not burn waste
Do not kill any wild
Report any chemical spills
Site vehicle to have spill kits
Store chemical only in the approved storage area where spill kit are available

## Slide 108: WASTE MANAGEMENT
WHAT IS WASTE MANAGEMENT ???..
Waste management - safely disposing the by-product of a process or a work to the environment ( after proper treatment, if necessary)
So that no threat for livings, properties and environment exists

## Slide 109: WASTE DISPOSAL
CLASSIFICATION OF WASTE
HAZARDOUS WASTE
NON-HAZARDOUS WASTE

## Slide 110: WASTE DISPOSAL
HAZARDOUS WASTE
Highly flammable waste
Chemical waste
Toxic waste
Corrosive waste
Electronic waste

## Slide 111: WASTE DISPOSAL
NON- HAZARDOUS WASTE
House waste
Food waste
Paper
Wood
Cotton

## Slide 112: WASTE DISPOSAL
SEGREGATION (பிரித்து வைத்தல்)
Waste must be segregated to prevent the mixing and contamination of one type of waste with another.
It usually requires separate as well as secure storage for each type waste with clear identification

## Slide 113: Movement
People Movement
Vehicle Movement

## Slide 114
MOVEMENT
OF
PEOPLE

## Slide 115: MOVEMENTS OF PEOPLE
Hazard: Slip Fall & Trip Fall
Cause of Slip Hazard
Smooth floor surface
Wet
Oil and Grease
Frost and Ice

## Slide 116: MOVEMENTS OF PEOPLE
Cause of Trip Hazard
Uneven or loose floor surface
Trailing cables
Object at floor

## Slide 117: MOVEMENTS OF PEOPLE
Control Measures
Good House Keeping
Risk Assessment
Maintenance of Machinery
Slip Resistance Surface
Spillage Control kit
Use of proper signage and PPE
Lay cables / Cable Rails
Designated Walk Ways

## Slide 118
MOVEMENT
OF
VEHICLE

## Slide 119: VEHICLE COLLISION
GLOBAL SAFETY STUDIES

## Slide 120: VEHICLE COLLISION
Collision can occur between the vehicle
Other Vehicle
Pedestrians
Fixed object

## Slide 121: VEHICLE COLLISION
Factors that increase the Risk of Vehicle Collision
Driver Error
Example: Driving Too Fast
Inadequate Lighting
Reversing with out the help of a banks man
Bad Weather Condition
Obstructed Visibility
Poor design of Pedestrian Walkways and Crossing point
Lack of Vehicle Maintenance
Example: Break Failure

## Slide 122: MAIN CAUSES OF ACCIDENT
ACCIDENT
Accident is an unplanned event that results Personal Injury or Property Damage or Equipment Damage or Environmental Pollution.
Unsafe Action
Unsafe Condition

## Slide 123: UNSAFE ACTION
Definition
Where the action of the people in the work place directly cause or contribute to the incident
Use wrong tools
Arranging or placing object unsafely
Using equipments unsafely
Operating without permission

## Slide 124: UNSAFE ACTION
Working At Unsafe Speed
Using Defective Equipment & Tools
Failure to use of PPE
Improper Lighting
Smoking
Horse Play
Not Using Safety Devices
Not Reporting Safety Problems
Working under the Influence of Alcohol

## Slide 125: UNSAFE ACTION

## Slide 126: UNSAFE CONDITION
DEFINITION
WHERE THE PHYSICAL CONDITION AT THE WORK PLACE, OR METHODS OF WORK, DIRECTLY CAUSE OR CONTRIBUTE TO THE INCIDENT
INADEQUATE GUARDING
DEFECTIVE TOOLS
INADEQUATE VENTILATION
EXCESSIVE NOISE

## Slide 127: UNSAFE CONDITION
NO PERSONAL PROTECTIVE EQUIPMENTS
WET AND SLIPPERY SURFACE
BAD HOUSEKEEPING
UNSAFE LIFTING
UNSAFE EQUIPMENTS
UNSAFE SYSTEM OF WORK
UNSAFE ENVIRONMENTAL CONDITIONS

## Slide 128: UNSAFE CONDITION

## Slide 129: DOMINO THEORY
88% of accidents due to unsafe action
10% of accidents due to unsafe condition
2% Unavoidable Accidents

## Slide 130: ELECTRICAL SAFETY
GLOBAL SAFETY STUDIES

## Slide 131: ELECTRICAL SAFETY
ELECTRICITY
Flow of electron in a conductor in a closed circuit
Flow of current only possible by voltage source

## Slide 132: ELECTRICAL SAFETY
ELECTRICAL HAZARD
PRIMARY HAZARD
SECONDARY HAZARD

## Slide 133: PRIMARY HAZARD (B-SAFE)
BURN
SHOCK
ARC FLASH
FIRE
EXPLOSION

## Slide 134: SECONDARY HAZARD
Person fall from height
Lose of information
Dropping of tool and objects
Unexpected movements of machinery
Health hazard due to release of Toxic Gas & Production of UV rays
Environmental Hazard

## Slide 135: ELECTRICAL SAFETY
Effects of Electrical Shock
Damage to nervous system
Irregular heart beat
Internal burns
Stop breathing
Skin surface burn

## Slide 136: ELECTRICAL SAFETY
Major Cause of Electrical fire
Overloading of circuit
Octopus wiring
Improperly rate circuit
Poor damage insulation
Poor connection
Flammable materials

## Slide 137: ELECTRICAL SAFETY
ELECTRICITY PROTECTIVE DEVICES
FUSE
EARTHING
ISOLATION
ELCB
MCB
RCD

## Slide 138: SAFETY ARRANGEMENTS
Proper Inspection
Use Distribution Board (DB)
All cable joints made with Industrial Plug
Give proper Earthling (Double Earthling)
Use proper PPE
Generator area to be cleaned properly
No flammable material near DG
Provide Extinguisher, Sign Board and Barricading around the DG
Don’t lay cables on wet area

## Slide 139: ELECTRICAL SAFETY
INDUSTRIAL PLUG.

## Slide 140: ELECTRICAL SAFETY
Emergency Action
Don’t touch the casualty
Call for help
Isolate from the power supply
Call for ambulance
Check for breathing
Treat burns
Treat for physical shock
Ensure medical assistance

## Slide 141: LOTO (LOCK OUT TAG OUT)

## Slide 142: LOTO
Definition
Lockout means physically neutralize all energies in a piece of equipment before beginning any maintenance or repair work.
Lock out generally involve , Stopping all energy flows and provide a tag to help
Isolation Types : Mechanical and Electrical

## Slide 143: LOTO- COLOUR CODE
ELECTRICAL DEPT - RED
MECHANICAL DEPT - YELLOW
INSTRUMENTATION DEPT - BLUE

## Slide 144: LOTO
DIFFERENT TYPES OF LOCKS

## Slide 145: ISOLATION
Electrical isolation is the separation between two circuits that restricts the Direct Current (DC) and any unwanted Alternating Current (AC) in a power supply.
Isolation prevents dangerous voltages to the operator in the event of an electrical fault/failure or during a surge from lightning.

## Slide 146: SCAFFOLDNG

## Slide 147: SCAFFOLDNG
DEFINITION
Scaffolding is a temporary elevated platform to do the height work safely
INTRODUCTION
It is estimated that 2.3 million construction workers deal with scaffolding each year. More than 10,000 workers are injured and 80 are killed in scaffolding related accidents

## Slide 148: TYPES OF SCAFFOLDS
Frame Scaffolding
Tube and Clamp Scaffolding
Modular System Scaffolding
Rolling Scaffolding (Mobile Scaffolding)
Suspended Scaffolding

## Slide 149: TYPES OF SCAFFOLDS
FRAME SCAFFOLDING

## Slide 150: TYPES OF SCAFFOLDS
TUBE AND CLAMP

## Slide 151: TYPES OF SCAFFOLDS
MODULAR SYSTEM SCAFFOLDS

## Slide 152: TYPES OF SCAFFOLDS
ROLLING SCAFFOLDING (MOBILE SCAFFOLDING)

## Slide 153: TYPES OF SCAFFOLDS
SUSPENDED SCAFFOLDIND

## Slide 154: TYPES OF SCAFFOLDING ( BASED ON WORKING LOAD)
LIGHT DUTY SCAFFOLD
MEDIUM DUTY SCAFFOLD
HEAVY DUTY SCAFFOLD
SPECIAL DUTY SCAFFOLD

## Slide 155: LIGHT DUTY SCAFFOLD
Scaffold designed and constructed to carry a working load not exceed 150kg/m2

## Slide 156: MEDIUM DUTY SCAFFOLD
Scaffold designed and constructed to carry a working load not exceed 200kg/m2

## Slide 157: HEAVY DUTY SCAFFOLD
Scaffold designed and constructed to carry a working load not exceed 250kg/m2

## Slide 158: SPECIAL DUTY SCAFFOLD
SCAFFOLD DESIGNED AND CONSTRUCTED TO CARRY SPECIFIC TYPE OF OBJECTS

## Slide 159: COMMON PARTS OF SCAFFOLD
Sole board/ sills
Base plate
Standard/ post
Ledger
Brace
Transom
Coupler
Working platform
Guard rails
Access ladder

## Slide 160: COMMON PARTS OF SCAFFOLD
SOLE BOARD/SILLS
SILVER OAK WOODEN PLANK SUPPORRT BASE PLATE AT GROUND.

## Slide 161: COMMON PARTS OF SCAFFOLD
BASE PLATE
IT IS A MILD STEEL SQUARE-PLATE

## Slide 162: COMMON PARTS OF SCAFFOLD
STANDARD/POST
IT IS VERTICAL SCAFFOLD TUBE

## Slide 163: COMMON PARTS OF SCAFFOLD
LEDGER
IT IS HORIZONTAL SCAFFOLD TUBE

## Slide 164: COMMON PARTS OF SCAFFOLD
BRACE
A TUBE PLACED TO THE VERTICAL AND HORIZONTAL MEMBERS OF A SCAFFOLD AND FIXED TO THEM TO GIVE STABILITY.

## Slide 165: COMMON PARTS OF SCAFFOLD
TRANSOM
TUBES FIXED AT RIGHT ANGLE ACROSS THE LEDGERS, ADJACENT TO EATCH PAIR OF STANDAEDS TO SUPPORT THE SCAFFOLD BOARDS

## Slide 166: COMMON PARTS OF SCAFFOLD
COUPLER
A DEVICE FOR LOCKING TOGETHER COMPONENT PARTS OF TUBE AND COUPLER SCAFFOLD .

## Slide 167: COUPLER
TYPES OF COUPLERS

## Slide 168: COMMON PARTS OF SCAFFOLD
WORKING PLATFORM
AN ELEVATED WORK SURFACE COMPOSED OF ONE OR MORE PLATFORM UNITS.

## Slide 169: COMMON PARTS OF SCAFFOLD
GUARD RAILS
TOP RAIL
MID RAIL
TOE BOARD

## Slide 170: COMMON PARTS OF SCAFFOLD
GUARD RAILS- HEIGHT
TOP RAIL
MID RAIL
TOE BOARD
 | 70 CM |  | TOTAL- 110 CM
 | 40 CM |  | 
 | 15 CM |  | 

## Slide 171: LADDER
Hazards of Ladders
Don’t stand ladder on drum, box or other unstable base
Never attempt to repair broken ladder
Never carry load up ladder hoist it up
When using the metal ladder, , make sure there are no electrical hazard in the near vicinity
Falling off the ladder

## Slide 172: LADDER
SAFE LADDER PLACING
Ladder should be set an angle of about 75 or one meter for every four meter rise

## Slide 173: LADDER
LADDER-SAFETY
Use only approved ladders
Inspect before use
One person only
Use fall arrest if > 6 ft (1.8m) working from ladder
Extend 3 feet above access or working level
use 4:1 lean ratio
Use 3 point contact

## Slide 174: LADDER
LADDER SAFETY

## Slide 175: LADDER
MONKEY LADDER

## Slide 176: HAZARDS - SCAFFOLDING
Fall from scaffold during erection
Fall from working platform
Electrocution- from overhead power lines
Falling object
Scaffold collapse

## Slide 177: CAUSE OF SCAFFOLD COLLAPSE
Over loaded working platform
Soft ground
Not tied properly with the building
Brazing insufficient
High wind
Incorrect copular
Scaffold erected by incompetent workers
Scaffold not inspected prior to use

## Slide 178: SAFETY ARRANGEMENTS -SCAFFOLD
Use appropriate scaffold construction method
Proper inspection
Trained and certified worker
Not exceed (SWL) Safe Working Load
Erection on a level ground
10 feet safe distance from power line
Proper fall protection system

## Slide 179: SCAFFOLD FALL PROTECTION SYSTEM
Guard Rail
Top Rail
Mid Rail
Toe Board
Training
Barricading
Full Body Harness
Safety Nets
Safety Monitoring
PFAS – Personal Fall Arrest System

## Slide 180: SCAFFOLD FALL PROTECTION SYSTEM
FULL BODY HARNESS

## Slide 181: FULL BODY HARNESS
PARTS OF HARNESS

## Slide 182: SCAFFOLD FALL PROTECTION SYSTEM
SAFETY NETS

## Slide 183: SCAFFOLD FALL PROTECTION SYSTEM
GUARD RAILS
TOP RAIL
MID RAIL
TOE BOARD

## Slide 184: SCAFFOLD INSPECTION CHECK LIST
Check For Missing Planks On Platform
Check For Missing Guard Rail System
Check For Proper Access
Check For House Keeping On Scaffold Platform (Loose Materials, Working Waste Etc…)
Check For Proper Tying Off Building

## Slide 185: SCAFF TAG SYSTEM
THREE TYPES OF SCAFF TAG
RED TAG – Don’t use
GREEN TAG – OK to use
YELLOW TAG – Check with Supervisor
If there is
NO TAG -
DON’T USE

## Slide 186: WORK AT HEIGHT
GLOBAL SAFETY STUDIES

## Slide 187: WORK AT HEIGHT
DEFINITION
Work there is a risk of fall liable to cause injury
Any work above 1.8 meter from ground level is called work at height

## Slide 188: WORK AT HEIGHT
RESULT OF FALLING FROM HEIGHT
FATALITY
SPINAL INJURY
MULTIPLE BROKEN BONES

## Slide 189: WORK AT HEIGHT
HAZARDS OF WORK AT HEIGHT
VERTICAL HEIGHT
FALLING METERIALS
WEATHER
UN PROTECTED EDGS
SLOPPING ROOFS

## Slide 190: WORK AT HEIGHT
CONTROL MEASURE FOR WORKING AT HEIGHT
TRAINING
BARRICATION
FULL BODY HARNESS
SAFETY NETS
PFAS-PERSONAL FALL ARREST SYSTEM
GUARD RAILS

## Slide 191: MANUAL HANDLING
GLOBAL SAFETY STUDIES

## Slide 192: MANUAL HANDLING
DEFINITION
Task which involves people moving or handling or shifting of materials by using bodily force
Example:
Lifting
Lowering

## Slide 193: MANUAL HANDLING
Manual Handling Hazards
Twisting and Turning
Heavy Load
Dropping Load
Sharp Edges
Hot Load

## Slide 194: MANUAL HANDLING
Manul handling injuries
Back injuries
Muscular sprain
Cuts and abrasion
Fracture
Open injuries
Swelling
Hernia

## Slide 195: MANUAL HANDLING TECHNIQUE
Assess the load
Position of feet
Bend knees
Leg muscle support
Back straight
Arm closed to the body
Avoid twisting

## Slide 196: EXCAVATION
GLOBAL SAFETY STUDIES

## Slide 197: EXCAVATION
Definition
Digging of earth surface or making depression on earth surface
Either manually or mechanically
What is Trench ?
Trench is a narrow excavation depth is greater than width

## Slide 198: EXCAVATION
Excavation hazard
Cave in
water accumulation
Oxygen deficiency
Toxic and flammable gases
Falling objects
People falling
Side wall collapse

## Slide 199: EXCAVATION
Preventive Measures
Proper inspection
Provide sign board
Barricading
Suitable side wall protection system (Sloping & Benching, Shoring, Shielding)
De-watering system
Proper PPE
Conduct gas test (O2, CO, H2S, Methane)
Removed soil , two feet from the side
Around traffic, use reflective vets
Access ladder

## Slide 200: EXCAVATION
EXCAVATION- SUITABLE SIDE WALL PROCTION SYSTEM
SLOPING
BENCHING SYSTEM
SHORING SYSTEM
SHIELDING SYSTEM

## Slide 201: EXCAVATION PROTECTION SYSTEM
sloping
A method of excavating in which the sides of an excavation are laid back to a safe angle to prevent cave-in

## Slide 202
BENCHING
A method of protecting employees from cave-ins by excavating the side s of an excavation to form one or a series of horizontal steps
EXCAVATION PROTECTION SYSTEM

## Slide 203
SHORING
Hydraulic, timber or mechanical system that support the sides of an excavation , designed to prevent cave-ins
EXCAVATION PROTECTION SYSTEM

## Slide 204
SHIELDING
A structure that is able to with stand the forces imposed on it by cave-ins, and in the process, protects employees inside the structure
EXCAVATION PROTECTION SYSTEM

## Slide 205: SITE CONDITION SHALL BE CHEKED BEFORE STARTING EXCAVATION
Traffic
Nearest structures and their condition
Soil test
Over head and under ground utilities ( Telephone lines, Electric lines, Water Lines, Other pipe lines )

## Slide 206: EXCAVATION
PREVENTION PEOPLE FALLING
Barricading and Toe board
Good light and sign
Crossing point
Access ladder
Ladder to extents 1 m above edges of excavation

## Slide 207: EXCAVATION
PROTECTION FROM VECHICLES
Fence or Barricading
Hand or Mechanical Signal
Stop Logs
Grade soil away from excavation
Good Light

## Slide 208: EXCAVATION
General tips
Any excavation or trench 4 feet or deeper shall be considered on a Confined Space
If the work around the Traffic Pedestrian Safety very important
A competent person inspect excavation on daily check adjacent area for possible cave-in failure of protective system and equipment, hazardous atmosphere or other hazardous condition.
Identify the under ground utilities by using Site Map, Utilities Detectors, Sign Board and Route Marks

## Slide 209: CONFINED SPACE
GLOBAL SAFETY STUDIES

## Slide 210: CONFINED SPACE
DEFINITION
Confined space has limited entry / exit, insufficient natural ventilation, lighting and not designed for continuous worker occupancy

## Slide 211: CONFINED SPACE
EXAMPLES OF CONFINED SPACES
STORAGE TANKS
MANHOLES
PIPE LINES
OIL PITS
WELLS
DUCTS
VESSELLS

## Slide 212: CONFINED SPACE
Hazards of confined space
Oxygen deficient atmosphere
Oxygen enriched atmosphere
Flammable atmosphere
Toxic atmosphere
Mechanical and Electrical Hazards
Engulfment hazards
High temperature
Wet surface
Falling objects
High Noise
Poisonous Creature

## Slide 213: CONFINED SPACE
Potential Hazards in Confined Space
Oxygen Deficiency
< 19.5% -23.5% oxygen concentration
Toxic Materials
Gasoline Fumes
Carbon Monoxide
Hydrogen Sulfide
Welding fumes
Corrosives

## Slide 214: CONFINED SPACE
Combustibles Materials
Methane
Hydrogen
Acetylene
Propane
Electricity or Mechanical Hazards
Mixer
Crusher

## Slide 215: CONFINED SPACE
ATMOSPHERIC HAZARDS
Oxygen deficiency
Oxygen enrichment
Combustible/ flammable materials
Toxic gases

## Slide 216: CONFINED SPACE
OXYGEN DEFICIENT ATMOSPHERES
19.5% | SAFE ZONE, MINIMUM FOR SAFE ENTRY
15-19% | DECREASED ABILITY TO WORK.
12-14 % | RESPIRATION INCREASES. POOR JUDGMENT
10-12% | RESPIRATION INCREASES. LIPS BLUE
8-10% | MENTAL FAILURE, UNCONSCIOUSNESS, VOMITING, NAUSEA
6-8% | DIFFICULT BREATHING, DEATH IN MINUTES
4-6% | COMA IN 40 SECONDS, DEATH

## Slide 217: CONFINED SPACE
Oxygen Enriched Atmosphere
Oxygen level above 23.5%
Causes flammable and combustible materials to burn violently when ignited
Never use pure oxygen to ventilate
Never store or place compressed tanks in a confined space

## Slide 218: CONFINED SPACE
General Hazards
Limited Access & Egress
Limited illumination and ventilation
Slip fall on wet surface
High temperature
Poisonous creatures

## Slide 219: CONFINED SPACE
Engulfment Hazards
Possibility of engulfment by flooding
Water or Sewage Flow
Loose, Granular Materials

## Slide 220: CONFINED SPACE
Mechanical and Electrical Hazards
Unexpected movements of mechanical equipments
Electric shock

## Slide 221: CONFINED SPACE SAFETY ARREGEMENTS
Check oxygen level, permissible is 19.5% to 23.5%
Check for flammable gases, below 10% of its LEL
Check the concentration of toxic gases available and measure with ppm
Proper ventilation and illumination
Isolate the space before entering
Worker must be trained and qualified
Provide a safety attendant out side
Use suitable PPE’S
use extra low voltage equipments (24V)

## Slide 223: CONFINED SPACE SAFETY ARREGEMENTS
Personal entry/ exit log sheet shall be maintained
For columns, tanks and other sludge contaminated confined spaces, first entry shall be with airline respirator only
All man ways shall be barricaded and no entry without permit sign shall be posted

## Slide 224: CONFINED SPACE SAFETY ARREGEMENTS
Mechanical ventilation
By using filtered compressed air
By using a blower fan
by using an exhaust fan

## Slide 225: CONFINED SPACE
WHO IS ENTRANT
THE EMPLOYEE WHO WILL PHYSICALLY ENTER THE CONFINED SPACE TO PERFORM THE WORK.WHO MUST BE TRAINED AND EXPERIENCED PERSON.

## Slide 226: CONFINED SPACE
WHO IS HOLE WATCHER/ SAFETY ATTENDANT
The attendant is the person stamp outside the confined space and is responsible for assisting the entrant in existing the confined space and calling for emergency assistance while required

## Slide 227: HOLE WATCH- DUTIES & RESPONSIBILITY
Check oxygen level
Check flammable gases
Check toxic gases
Personal entry/ exit log sheet shall be maintained
Permit available on location and check validity
Rescue procedure discussed with workers
Air supply availed on location
Proper ventilation and illumination
Use extra low voltage equipments
All man ways shall be barricaded and no entry with out permit sign shall be posted
All recommended PPE’s are used

## Slide 228: CONFINED SPACE
Confined space- general tips
There should be good communication between entrant and attendant
Conduct the gas test every hour and test all area of confined space top, middle, and bottom of this space.
Because some gas heavier than air some gas light than air .
Common chance toxic gases in confined space are CO and H2S

## Slide 229: H2S HYDROGEN SULPHIDE
GLOBAL SAFETY STUDIES

## Slide 230: H2S - HYDROGEN SULPHIDE
Definition
It is mainly formed by chemical reaction and biological decomposition
H2S is one of the dangerous natural gases
Industrial Sources Of H2S
Gas Processing, Oil/ Gas Production & Drilling Rigs, Hydrocarbon Refining, Oil Storage Tanks, Sewage Treatment Plants, etc.

## Slide 231: H2S- HYDROGEN SULPHIDE
Properties of H2S
Toxicity
Colorless
Rotten egg smell
Heavier than air
Flammability
Solubility
Corrosives
H2S is dispersed by the wind

## Slide 232: H2S- HYDROGEN SULPHIDE
Emergency / First Aid Measure
Inhalation:
Remove the victim to fresh air area, provide artificial respiration or oxygen if needed.
Eyes:
Irrigate with plenty of water for 15 min.
Skin:
Remove the contaminated clothing and wash the affected area with plenty of water and soap.
Seek medical aid immediately

## Slide 233: SO2 - SULFUR DIOXIDE
Properties Of SO2
Highly Toxic
Colorless
Heavier than H2S and Air
Highly Corrosive
Non-flammable

## Slide 234: H2S TOXICITY TABLE
H2S concentration | effect On victim
Less than 1 ppm | Detectable by smell
10 ppm | Possible headache
Above 30 ppm | Eye & Respiratory irritation
Above 100 ppm | Loss of sense of smell
Above 500 ppm | Dizziness, Nausea, Abdominal Pain
700 to 1000 ppm | Rapid unconsciousness
Above 1000 ppm | Rapid collapse and death

## Slide 235: TYPES OF GAS DETECTORS
Portable Multi-gas Detectors
Area Multi-gas Detectors
Personal H2S Gas Monitor
Fixed Gas Detectors

## Slide 236: GAS DETECTORS
Portable Multi Gas Detectors
Portable gas detectors are fitted with electro chemical sensors and used to test Oxygen, Toxic, and Flammable gas levels in the work to comply with the permit to work.
The detector produces an Audible Alarm, Flashing Visual Alarm and Vibrating Alarm on gas detection at TLV or above.

## Slide 237: GAS DETECTORS
Area Multi Gas Detectors.
It is used as a single unit or linked together for area protection .
Monitor levels of Oxygen, Methane, H2S, and Carbon monoxide (CO)

## Slide 238: GAS DETECTORS
Personal H2S Gas Monitor
Personal H2S gas monitor is maintenance free and calibration free, disposable single gas monitor.
Disposed every two years
The gas monitor produces Audible Alarm, vibration, and bright flashing visual alarm on H2S detection at 10 ppm or above.
Note : Personal H2S gas monitor should not be used for gas testing

## Slide 239: GAS DETECTORS
Fixed Gas Detectors
Fixed gas detectors are used to monitor H2S.
This can be linked to control room by which, we can identify the exact location of detection

## Slide 240: TOOLS
GLOBAL SAFETY STUDIES

## Slide 241: TOOLS
TYPES OF TOOLS
Hand Tools
Power Tools
Pneumatic Tools

## Slide 242: TOOLS
Common Hazards
Electric Shock
Flash Burns
Falling
Hand and Eye Injuries
Cut or losing a body parts
Ergonomic injuries

## Slide 243: TOOLS
Basic Tools Safety Rules
Maintain Regularly
Use right tools for the Right Job
Inspect before use
Operate according to manufacture instruction
Use the right PPE
Use Guards

## Slide 244: TOOLS
Hand Tools
Some examples
Hammers
Screwdrivers
Cutters
Spanners
Hand Tools Hazard
Hazards are usually caused by Misuse and Improper Maintenance

## Slide 245: TOOLS
Hand Tools - Safety Tips
Right tools for the right job
Good condition
Proper care and maintenance
Use proper PPE
Avoid use of Mushroomed Hammer and Chisel

## Slide 246: TOOLS
Power Tools
Tools which are run by (electricity) electrical power supply is known as Power Tools
Electrical Drills
Electrical Grinder
Jig Saw
Electrical Cutter
Power Tool Hazards
Electrical Shock
Cut or losing of body parts
Broken Bones
Hit

## Slide 247: TOOLS
Power Tools – Safety Tips
Cable, Plugs are in good condition
Tools use with correct power supply
Make sure power supply to be properly earthed
Tools must be switched off before plug in
Use proper PPE
Keep tools clean and dry
Disconnect when not in use
Proper inspection and maintenance

## Slide 248: TOOLS
Safety Tips - Angle Grinder
Disc RPM must be GREATER than grinder machine RPM
Validity date - do not use in case of expiry
Angle Grinder & Disengaged Disc injuries

## Slide 249: TOOLS
Pneumatic tools
Powered by compressed air includes Chipper, Drills, Sander.
Pneumatic tools hazards
Main hazard is getting hit by tools
Noise is an other hazard

## Slide 250: TOOLS
Pneumatic Tools – Safety Tips
Authorized operator
Regularly maintained and serviced
Protective guard is correctly fitted before use
Proper PPE
Turn off the compressed air main supply before disconnecting
Leakage of air shouldn’t touch by hands
Never use body for cleaning
Keep the tool in horizontal position when changing bits or points

## Slide 251: FIRST-AID
GLOBAL SAFETY STUDIES

## Slide 252: FIRST-AID
In the event of an accident, you should act in the following way;
Prevent more people from being injured
Call the Supervisor or the Person Responsible for First Aid Treatment. Call ambulance if necessary
Aid the injured person

## Slide 253: FIRST-AID
AIM OF FIRST AID
Preserve Life
Prevent Deterioration (Condition is Worsening)
Promote Recovery
CPR- Cardio Pulmonary Resuscitation
C: compressions
A: airway
B: breathing
Remember to spell C-A-B

## Slide 254: WELFARE FACILITIES AT SITE
Management must provide welfare facilities to the workers
Toilets
Washing Facilities
Drinking Water
Rest Room
Prayer Hall
Smoking Area
First Aid Facilities
Facilities for Intake of Meals

## Slide 255: PERMIT TO WORK
GLOBAL SAFETY STUDIES

## Slide 256: PERMIT TO WORK
DEFINITION
Legal Document
Formal written statement of work
Important fields in PTW:
Hazard
Risk
Safety Precautions / Control Measures
Confirmation
Work Permit is an Important Accident Prevention Tool

## Slide 257: PERMIT TO WORK
WHAT IS WORK PERMIT SYSTEM ???
specifies the work to be done and the precautions to be taken
Work permit is an essential part of Safe System of Work (SSoW) in many maintenance activities

## Slide 258: PERMIT TO WORK
TYPES OF WORK PERMIT
Hot Work Permit
Cold Work Permit
Confined Space Entry Permit
Electrical Work Permit
Radiography Permit
Vehicle , Machinery Permit
Road Close Permit
Excavation Permit

## Slide 259: PERMIT TO WORK
Permit Checklist
Permit Number :
Work Request :
/ Work Description
Hazards/ Dangers :
Precautions required :
Isolation Details :
Purging System :
Site Preparation :
Protective & Safety Equipment :

## Slide 260: PERMIT TO WORK
Associated Permits / Certificates
Gas Test - Authorised Gas Tester
Sign for Permit Controller, Performing Authority, Work Site Supervisor
Permit Controller Shift Change / Transfer Endorsement
Area Authority Endorsement

## Slide 261: PERMIT TO WORK
Supporting Documents PTW
Work Method Statements
Job Safety Analysis
Risk Assessment
Training Reports
Third Party Certificate
PTW Checklist
Area Drawing

## Slide 262: FORK LIFT
GLOBAL SAFETY STUDIES

## Slide 263: FORK LIFT
Factors that may cause a forklift truck to Overturn
Driving around corners too quickly
Uneven loading of the fork
Driving with the Load Elevated , Especially when going around Corners
Uneven Tyre Pressure
Excessive Breaking
Driving across a Slope rather than straight up or down the slope
Collision , especially with kerbs

## Slide 264: FORK LIFT

## Slide 265: FORK LIFT
Forklift Safety
Use safe speed
Be aware of fork position
Watch out the blind spots (use blind Spot Mirror)
Slow down and sound horn at the corner
Certified forklift operators only
Inspect the forklift before shift change

## Slide 266: FORK LIFT
Pre - use – check – forklift
Tyre pressure
Parking Brakes
Steering
Fuel, Oil and Water System for Leak
Batteries
Lifting and Tilting System
Audible Warning
Lights
Mirrors

## Slide 267: FORK LIFT
Parking rules for a forklift
Apply the hand break
Lower the fork and tip the forward
Remove the key
Park it on level area
Do not obstruct traffic
Do not obstruct the pedestrian walkways
Do not obstruct the emergency escape routes

## Slide 268: CRANE & LIFTING EQUIPMENT
GLOBAL SAFETY STUDIES

## Slide 269: CRANE
Crane is a mechanical device used to handle the load, materials, structure for lifting and distributing.
TYPES OF CRANES
MOBILE CRANE
HYDRAULIC CRANE
OVERHEAD CRANE
GANTRY CRANE
TOWER CRANE

## Slide 270: MOBILE CRANE

## Slide 271: HYDRAULIC CRANE

## Slide 272: OVERHEAD CRANE

## Slide 273: GANTRY CRANE

## Slide 274: TOWER CRANE

## Slide 275: CRANE & LIFTING
CRANE & LIFTING PTW
Traffic permit
Method statement
Job safety analysis
Training report
Area drawing
Lifting plan
Third party certificates
Equipments certificates
Other certificates

## Slide 276: CRANE
MAJOR CAUSES OF CRANE ACCIDENTS
Contact with power lines
Overturns
Fall of material
Mechanical failures

## Slide 277: CRANE
HOW DO ACCIDENTS OCCUR
Instability
Unsecured load, Load Capacity Exceed, or Ground not level or too soft.
Lack of communication
Point of the operation is a distance from the crane operator or not in full view of the operator
Lack of Training
Inadequate Maintenance or Inspection

## Slide 278: CRANE & LIFTING PARTS

## Slide 279: CRANE & LIFTING
Crane hazards
Improper load rating
Excessive speeds
No hand signals
Inadequate inspection and maintenance
Unguarded parts
Unguarded swing radius
Working too close to power lines
Shattered windows
No steps/ guard rails walkways
No boom angle indicator
Not using outriggers

## Slide 280: CRANE & LIFTING
Crane Operation- Safety Arrangement
Proper Inspection
Trained operator with valid License
Valid Third Party Certificate of all lifting gears
Proper Barricading and Sign Board
Load Rating Chart & Operating Manual in the cabin
Never exceed Safe Working Load (SWL)
6m distance from power line
Experienced Riggers team

## Slide 281: CRANE & LIFTING
Crane Operation- Safety Arrangement
Daily inspection of lifting gears
Proper communication & signals
Use tag line , if necessary

## Slide 282: CRANE & LIFTING
Who is Rigger Supervisor?
Rigger supervisor is a person who has overall control of lifting operation , must be trained and experienced

## Slide 283: CRANE & LIFTING
Rigging Equipments & Slings
Wire rope
Fiber rope
Synthetic web sling
Wire rope web sling
Chain block
D- shackles
I- bolts
Liver hoist ( chain puller)

## Slide 284: CRANE & LIFTING
Rigging Equipments & Slings

## Slide 285: CRANE & LIFTING
COLOUR CODE – WEB SLINGS
1 TON | VIOLET
2 TON | GREEN
3 TON | YELLOW
4 TON | GRAY
6 TON | BROWN
10 TON | RED

## Slide 286: CRANE & LIFTING
Crane Operation- Safety Tips
Never walk or stand under any suspended load
All signal must be received from authorized signal man (Rigger)
Bad Weather – stop lifting ( high wind and rain)
Third party certification for all lifting equipments

## Slide 287: MATERIAL STORAGE
GLOBAL SAFETY STUDIES

## Slide 288: MATERIAL STORAGE
Prevention of Falling of Materials from Material Stack
Stacking of Materials
Stack materials separately
Maximum height for stacking
Stack vertically
Use pallets
Allow sufficient space around stacks
Protect stack from being struck by vehicles

## Slide 289: MATERIAL STORAGES
Safe Storage Materials
Separate storage area for materials
Area should be kept clean and tidy
Warning sign
Flammable liquids and gases should be stored separately
Store made of fire resistant materials
Keep Ignition Source Away
Fire Fighting Equipments
Regular Inspection

## Slide 290: MATERIAL STORAGES
Safe stacking and storage of flammable materials
Liquids, solids, gases in separate storage
Storage oxygen separate from other gases
Fire – resistance internal storage
Warring sign / safety sign
No hot work in near storage area
Fire fighting equipments provided
Inspect regularly
Correctly rated electrical equipments

## Slide 291: MATERIAL STORAGES
Safety Rules - Oxygen Cylinder
Oxygen cylinder should not be kept near combustible materials
Oxygen cylinder should not be handle with greasy hands or gloves
Oxygen cylinder their fitting should not be tested with oil based soap solution
Top cover of the cylinder should be kept in position and screwed safety when not in use
Cylinder should not be used as rollers for moving materials

## Slide 292: HOT & COLD ENVIRONMENT
GLOBAL SAFETY STUDIES

## Slide 293: HOT & COLD ENVIRONMENT
Effect of Exposure to Extreme Heat
Hyperthermia - Dehydration
Muscle Cramp
Heat Stress - Increases Discomforts, Headache
Heat Stroke
Skin Burn, Skin Cancer

## Slide 294: HOT & COLD ENVIRONMENT
EXPOSURE OF COLD ENVIRONMENT
Frost Bite
Slip Hazard
Freeze Burn Injury

## Slide 295: HOT & COLD ENVIRONMENT
CONTROL MEASURES
HOT ENVIRONMENT
Ventilation
Insulation
Cool refuges
Drinking water
Appropriate clothing
Job rotation

## Slide 296: HOT & COLD ENVIRONMENT
Cold Environment
Close Ventilation
Warm Refuges
Hot Food and Drinks
Job Rotation
Remove Ice
Insulating Jackets

## Slide 297: ACCIDENT / INCIDENT REPORTING
GLOBAL SAFETY STUDIES

## Slide 298: ACCIDENT REPORTING
ACCIDENT
Accident is an unexpected event or unplanned event that results personal injury or property damage or equipment damage or environmental pollution.

## Slide 299: ACCIDENT REPORTING
Benefits of Accident Reporting & Investigation
Preventing reoccurrence
Identifying out- dated procedures
Improved work environment
Increased procedures
Raises safety awareness
Increased reputation & Morale
Benefits to all…..

## Slide 300: ACCIDENT REPORTING
What should be reported?
All injuries or Job Related Illnesses
Near-miss incidents
Equipment damage
Potentially unsafe condition
Potentially unsafe action

## Slide 301: ACCIDENT REPORTING
Accident Report Content (Sample)
Department -
Supervisor Name -
Date of Accident -
Time of Accident -
Name of Injured Person -
Works Number -
Reason for Accident -
Witnesses -
Corrective Action -
Recommendations -

## Slide 302: JOB SAFETY ANALYSIS (JSA)
GLOBAL SAFETY STUDIES

## Slide 303: JOB SAFETY ANALYSIS - (JSA)
Definition
JSA is a carful study of each step in a job, identifying the hazards in each step individually and giving appropriate control measure to reduce the risk

## Slide 304: JOB SAFETY ANALYSIS (JSA)
JSA STEPS
STEP - 1 - Break the Job in to Basic Steps
STEP - 2 - Hazards Identification
STEP - 3 - Control Measure

## Slide 305: JOB SAFETY ANALYSIS (JSA)
select job | job step | hazard Identification | Control Measure
projector installation | Materials arrangement | Lack of awareness, Supervision, Trip & Fall | awareness for manual handling, good house keeping, qualified supervisor
 | working plat form construction & dismantling | Unskilled labors, Improper Supervision | Trained & competent worker & supervisor, effective scaffold safety procedure

## Slide 306: JOB SAFETY ANALYSIS (JSA)
Select job | Job Step | Hazard identification | Control measure
 | Projector mounting | Standard power tools, Lack of training, Supervision | All power tool must be in good condition and inspect well, follow proper installation method

## Slide 307: JOB SAFETY ANALYSIS (JSA)
It helps to inspect the plant
It helps to identify hazard and prevent accident
It helps to establish safe work method, working condition.

## Slide 308: EMERGENCY PLANNING

## Slide 309: EMERGENCY PLANNING
Emergency planning helps to safe guard people and provide information to media.
It helps to avoid confusion and loss

## Slide 310: ASSEMBLY POINT
A designated place where people have been told to wait after evacuation of the building during fire or other emergency situations

## Slide 311: EVACUATION PROCEDURE
Sound of alarm
Get out of the building
Stay out of the building ( Assembly Point)

## Slide 312: EVACUATION PROCEDURE
SOUND OF ALARM

## Slide 313: EVACUATION PROCEDURE
Get out of the building
No use of lift
more than two separate routes may be required
Stairs, corridors and door are fire resistant protection
Doors open in the direction of travel
Travel distance should be short
Adequate width
Clearly signed
Emergency lights
No obstruction

## Slide 314: EVACUATION PROCEDURE
Stay out of the building ( Assembly Point)
Safe distance from the building
Safe location
Further escape possible if needed
Clearly signed

## Slide 315: MOCK DRILL
A mock drill is a method of practising how a building would be evacuated in the event of a fire or other emergency situations

## Slide 316: ERGONOMICS
GLOBAL SAFETY STUDIES

## Slide 317: ERGONOMICS
Definition
Study of relationship between worker, work, work position (equipment & environment)
Equipment or Tools or Machinery - they are using
(Example: Computer - IT company)
Work Place Environment
(Example: Suitability of Lighting)

## Slide 318: ERGONOMICS
Asbestos Dust - Asbestosis
Vibration - Vibration White Finger
Sitting for too long - Back Pain, Neck Ache
Lack of lighting - Headache, Eye Strain

## Slide 319: ERGONOMICS
IT Professional Health & Safety
An ergonomically study about computer users health problems & safe operation
Potential Health Effects
Body Fatigue
Upper Limb Pains and Discomfort
Eye Strain
Headaches
Neck Ache
Stress & Fatigue

## Slide 320: ERGONOMICS
GOOD ERGONOMIC WORK STATION

## Slide 321: HOT WORK
GLOBAL SAFETY SYUDIES

## Slide 322: HOT WORK
Definition
Any work which uses Naked Flame or any source of ignition generation such as Heat or Spark is called Hot Work

## Slide 323: SOURCE OF IGNITION
Sparks from Electricity
Smoking
Naked Flame
Hot Surface
Sparks from Vehicles
Lightning
Static Electricity
https://www.youtube.com/watch?v=XKAhx4NdJTs

## Slide 324: HOT WORK
Safety Arrangements / Control Measure
Booth Preparation
Proper Inspection
Check the Hot Work Permit
Test for Oxygen Level
Test for LEL
Trained/ Experienced Worker
Proper Supervision (Fire Watcher)
Keep Combustible Material Away
Suitable Extinguisher
Proper Ventilation & Illumination
Proper Housekeeping (5s rule)

## Slide 325: HOT WORK
Inspect Tools and Equipment
Electric Device - insulated and earthed
Gas Cylinder - up right position
Gas Regulator and Pressure Gauge - good condition
Flash Back Arrestor
First - Aid Kit
Barricade and Sign Board

## Slide 326: FIRE WATCH
Definition
Look out person assigned in hot work job – Fire Watcher
Hot Work Job Example
Welding
Cutting
Grinding

## Slide 327: HOT WORK
Fire Watcher - Duties And Responsibility
Make sure flammable materials and explosive materials are not in the work place
Check the Hot Work Permit
Check that area cleaned or not
Check area for No Hot Work Sign and other Posted Danger Marking
Know exact location of Acetylene and Oxygen shut off valve
Test for Oxygen Level and LEL level
Ensure the condition of Fire Hose, Fire Extinguisher and Fire Blanket

## Slide 328: HOT WORK
Check to see that there is adequate ventilation
Know the location fire alarm and emergency telephone
Check the Barricade & sign board availability
Locate emergency exits and make sure they are free of obstruction

## Slide 329: COLD WORK
Definition
The work which does not involve source of ignition or naked flame or spark or heat generation is called cold work
Example:
Scaffolding , Housekeeping, Manual Handling

## Slide 330: DEMOLITION
GLOBAL SAFETY STUDIES

## Slide 331: DEMOLITION
Definition
Demolition means total destruction and dismantling of the structures.

## Slide 332: DEMOLITION
Demolition Hazards
Premature collapse
Work at height
Live Over Heads
Asbestos
Dust
Explosive
Manual handling
Biological hazard
Sharps edges

## Slide 333: DEMOLITION
Control Measures
Structural surveys
Hazardous materials removed
Change of method to reduce people
Security for the site
Damping down to Minimise Dust (with water )
Disconnection of services

## Slide 334: MATERIAL SAFETY DATA SHEETS (MSDS)
GLOBAL SAFETY STIUDES

## Slide 335: MSDS
What is an MSDS ???
Material Safety Data Sheet
Developed by chemical manufacturers and importers
MSDS must be on hand for each hazardous chemical used by the company

## Slide 336: MSDS
Where are your MSDS
MSDS….
Must be readily accessible to employees during their work shift (Day / Night / General)
Typically kept in centralized location
Must be updated as new information becomes available

## Slide 337: MSDS
What information is on MSDS ?
Chemical Name
Manufacture Info ( Name, Address, Telephone)
List of Ingredients
Hazard Identification
FIRST-AID measure
FIRE- FIGHTING measure
Handling and Storage
Controls and Personal Protection
Transport Information

## Slide 338: RISK ASSESSMENT
GLOBAL SAFETY STUDIES

## Slide 339: RISK ASSESSMENT
RISK
It is the probability of the realization of the potential for loss.
RISK ASSESSMENT
Process of identifying hazards and evaluating the risk.
HOW MANY PROCESS STEPS IN RA?

## Slide 340: RISK ASSESSMENT
Risk Assessment – 5 Step Process
Identify the hazards
Identify the people who might be harmed and how might be harmed
Evaluate the risk
Record the significant finding
Review and Update

## Slide 341: RISK ASSESSMENT
HAZARD IDENTIFICATION METHODS
Inspection
Task Analysis
Legislation
Manufacturers Information (MSDS)
Incident / Accident Data

## Slide 342: RISK ASSESSMENT
IDENTIFYING THE PEOPLE AT RISK
Worker/ Operator
Maintenance Staff
Cleaners
Contractors
Visitors
Members of the public

## Slide 343: RISK ASSESSMENT
EVALUATE THE RISK
RISK= LIKELIHOOD CONSEQUENCE
What is Evaluation?
By assigning score value to Likelihood and Consequence - risk rating can be calculated
Example:
LIKELIHOOD | CONSEQUENCE
1= Extremely Unlikely | 1= Very Minor Injury
2= Unlikely | 2= First Aid Injury
3= Possible | 3= Lost Time Injury
4= Likely | 4= Hospital Treatment
5= Very Probable | 5= Disabling Injury

## Slide 344
RISK ASSESSMENT
Consequence

## Slide 345: RISK ASSESSMENT

## Slide 346: RISK ASSESSMENT
A construction company use the following time scales in relation to the risk rating system.
Risk Rating | Action and Time Scale
16 and above | unacceptable work may not started ,additional control must be introduced to reduce below 9.
9 to 15 | Tolerable additional control must be introduced as soon as possible and no later than 24 hours after assessment.
5 to 8 | Tolerable must be reduce to below 5 within one week
4 or below | Acceptable if simple action can reduce further then must be done within one week.

## Slide 347: RISK ASSESSMENT
Recording Significant Findings
Significant findings of a risk assessment should be recorded to provide a statement of the hazard in the workplace, the extent of the risks that they present, and the action taken to control those risks.

## Slide 348: GOAL TO IMPROVE SAFETY
Good house keeping at work site
Increase good citizens by 100 % PPE
Job wise risk identification
Reporting near miss, unsafe acts/condition
100% plant specific training and medical
Learning from incident/accident
Mobile phone restriction in the plant area
Zero accident/incident
Daily and weekly toolbox talk
Weekly/monthly hand tool inspection
Monthly inspection of PPE

## Slide 349: GOAL TO IMPROVE SAFETY
Monthly internal safety audit
New employees job related training and safety induction training
Behaviour change in technicians towards work safety
Implementation of awarding system

## Slide 350: SAFETY DOCUMENTS
Project Plan File
Safety Induction Details
Tool Box Talk Report
Daily Observation Report
Observation Closeout Report
Safety Inspection Report
Project JSA/ RA
Accident/ Incident Report
Near Miss Report
First Aid Report
Third Party Certificate
Calibration Certificate

## Slide 351: SAFETY DOCUMENTS
Insurance certificate
Medical certificate
Weekly HSE report
Work method statement
Close out PTW
MSDS file
Mock drill report
Waste disposal record

## Slide 352: SAFETY PROMOTIONAL ACTIVITIES
TRAINING PROGRAM ( SAFETY INDUCTION, TBT Etc…)
SAFETY NOTICE BOARD
SAFETY BANNERS
SAFETY STICKER
SAFETY SIGN
SAFETY SLOGANS
SAFETY AWARDS
MOCK DRILLS

## Slide 353: SAFETY PROMOTIONAL ACTIVITIES
SAFETY SLOGANS

## Slide 354: HELICOPTER ANATOMY

## Slide 355: ABBREVIATIONS
SAFETY- STAY ALERT FOR EACH TASK YOU DO
FIRE - FIND INFORM, RESTRICT,EXTINGUISH
HSE - HEALTH SAFETY ENVIRONMENT
OSHA - OCCUPATIONAL SAFETY AND HEALTH ADMINISTRATION
IOSH -INSTITUTION OF OCCUPATIONAL SAFETY AND HEALTH
NEBOSH- NATIONAL EXAMINATION BOARD IN OCCUPATIONAL SAFETY AND HEALTH
NFPA - NATIONAL FIRE PROTECTION ASSOCIATION
NSC - NATIONAL SAFETY COUNCIL
NBC -NATIONAL BUILDING CODE
PTW - PERMIT TO WORK

## Slide 356: ABBREVIATIONS
TBT - TOOL BOX TALK
RA - RISK ASSESSMENT
TRA - TASK RISK ASSESSMENT
HIRA - HAZARD IDENTIFICATION RISK ASSESSMENT
JSA - JOB SAFETY ANALYSIS
JHA - JOB HAZARD ANALYSIS
NM - NEAR MISS
FAK - FIRST AID KIT
FAC - FIRST AID CASE
LTI - LOST TIME INJURY
PPM - PARTS PER MILLION
HID - HAZARD IDENTIFICATION

## Slide 357: ABBREVIATIONS
DCP - DRY CHEMICAL POWDER
FMB - FOAM MAKING BRANCH
AFFF - AQUEOUS FILM FORMING FOAM
LOTO - LOCKOUT AND TAGOUT
CPR - CARDIO PURLMINORY RESUSCITATION
PASS - PULL AIM SQUEEZE SWEEP
STOP - SAFETY TRAINING OBSERVATION PROGRAMME
HAZOP- HAZARD AND OPERABILITY ANALYSIS
NRV - NON RETURN VALVE
MSDS - MATERIAL SAFETY DATA SHEET

## Slide 358: ABBREVIATIONS
SCBA - SELE CONTAINED BREATHING APPARATUS
CABA - COMPRESSED AIR BREATHING APPARATUS
LEL - LOWER EXPLOSIVE LIMIT
UEL - UPPER EXPLOSIVE LIMIT
PEL - PERMISSIBLE EXPOSURE LIMIT
STEL - SHORT TERM EXPOSURE LIMIT
ILDH - IMMEDIATE DANGER TO LIFE OR HEALTH
SWL - SAFE WORKING LOAD
PFAS - PERSONNEL FALL ARREST SYSTEM
ELCB - EARTH LEAKAGE CIRCUIT BREAKER
GFCI - GROUND FAULT CIRCUIT INTERRUPTER
MCB - MINIATURE CIRCUIT BREAKER