## Slide 1: DIPLOMA IN FIRE & SAFETY ENGINEERING (BSS- APPROVED BY GOVT OF INDIA)
(An ISO 9001-2008 Certified Safety Training and Consulting Organization)

## Slide 2: NATIONAL SAFETY DAY – 4TH MARCH NATIONAL FIRE DAY- 14TH APRIL

## Slide 3: WHY SAFETY ???
GLOBAL SAFETY STUDIES

## Slide 4: WHY SAFETY???
MORAL
LEGAL
ECONOMIC & FINANCIAL

## Slide 5: MORAL
BY THE CONSIDERING THE HUMANITARIEN REASON THE EMPLOYER HAVE THE MORAL RESPONSIBILITY TO PROVIDE SAFE & HEALTH WORK PREMICS , EQUIPMENTS & GOOD WORKING CONDITIONS..

## Slide 6: LEGAL
AS PER THE LAW THE ORGANIZATION SHOULD FULL FILL THE LEGAL REQUIREMENT TO AVOID THE LEGAL PROTECTION LIKE COMPENSATION AND IMPRISONMENT ETC…

## Slide 7: ECONOMICAL & FINANCIAL
WHEN THE ACCIDENT OCCURE THEIR WILL BE DIRECT AND INDIRECT COST ASSIGHNED WITH THAT EVENT..
DIRECT COST
INDIRECT COST

## Slide 8: DIRECT COST
THE MESSURABLE COAST ARISING DIRECTLY FROM THE ACCIDENT.
DIRECTLY FROM THE ACCIDENT
FIRST AID COST
MEDICAL TREATMENT COST
COMPENSATION COST

## Slide 9: INDIRECT COST
CANNOT BE MESSURED WHICH ARISED INDIRECTLY AS THE CONSEQUENS OF THE EVENT..
SALARY TO INJUIRED PERSON
REPLACEMENT WORKERS
TRAINING FOR NEW WORKERS
INVESTIGATIONS
LEGAL FEES
CLEANING COST
REPAIR OF PLANT

## Slide 10: HSE
H- HEALTH
S- SAFETY
E- ENVIRONMENT

## Slide 11: HEALTH
HEALTH IS A STATE OF COMPLETE PHISICAL, MENTAL AND SOCIAL WELL BEING NOT MERELY THE ABSENCE OF DISDASES OR INFIRMITY

## Slide 12: SAFETY
SAFETY CAN BE DEFINED AS FREEDOM FROM THEIR CONDITION THAT CAN CAUSE INJURY OR DEATH TO PERSONAL DAMAGE OR LOSS OF EQUIPMENT AND PROPERTY

## Slide 13: ENVIRONMENT
ENVIRONMENT MEANS THE SURROUNDING IN WHICH AS ORGANIZATION OPERATE INCLUDING AIR, WATER, LAND, NATURAL RESOURES, FLORA HUMAN AND THEIR INTER RELTIONSHIP.

## Slide 14: DUTIES & RESPONSIBILTIES OF HSE OFFICER….
ENSURING COMPLANCE WITH RESPECT TO HEALTH, SAFETY, ENVIRONMENTAL AS PER THE COMPANY, PROJECT HSE PLAN & STATUTORY REGULATION.
ENSURING & MONITORING IMPLEMENTATION OF HSE POLICY & PLAN
INTRACTING & CORDINATING WITH CLIENT AND OTHER AGENCIES IN CONNECTION WITH HSE.
MONITORING SAFETY PROCEGURE PRACTICE & THEIR COMPLAINTS
ENSSURE AND MONITOR THAT ALL PERSONAL UNDERSTAND THEIR HSE RESPONSIBILITIES

## Slide 15
6. CONDUCTING AND ORGANIZING HSE TRAINING
PROGRAMME
7. CONDUCTING INTERNAL SAFETY AUDIT, SAFETY
MEETING, MOCK DRILL, EMERGENCY EVACUTION
DRILL ETC..
8. ORGANIZING HSE PROMOTIONAL ACTIVITIES
9. ACCIDENT INVESTIGATION REPORTING AND
RECORDING
10. INSPECT THE WORK PLACE TO IDENTIFY HAZZARD
AND REPORT THE FINDING WITH
RECOMMENDATION FOR CURRECTIVE ACTION
TO THE SITE MANAGEMENT. PERIODICALLY
INSPECTION OF FIRE AND SAFETY
EQUIPMENTS

## Slide 16
PREPAIRING UPDATING COMPANY SAFETY
MANNUAL, HSE PLAN, JOB SAFETY PLAN, JOB
SAFETY ANALYSIS, SITE SAFETY RULES,
EMERGENCY PLAN ETC..
12. ENSSURE THE AVAILIBILITY AND QUALITIES OF
PPES
13. GUIDING AND ADVAISING LATEST HSE NORMS
AND REGULATIONS TO THE MANAGEMENT.
14. TO COORDINATE AND MAINTAINE WASTE
MANAGEMENT SYSTEMS
15. DISCUSS THE SAFETY ISSUE WITH THE
MANAGEMENT DURING WEEKLY OR MONTHLY
MEETING..

## Slide 18: FIRE
FIRE IS CHEMICAL CHAIN REACTION BETWEEN FEUL HEAT AND OXYGEN

## Slide 19: CLASSIFICATION OF FIRE
 | DESCRIPTION | EXAMPLE
A (SOLIDS) | FIRE INVOLVING ORDINORY COMPUSTABLE MATERIALS | WOOD, PAPER, TEXTILES ETC..
B (LIQUIDS) | FIRE INVOLVING FLAMMABLE LIQUIDS OR LIQUEFIABLE SOLIDS | PETROLIUM PRODUCTS, PAINTS ETC..
C (GASES) | FIRE INVOLDING GASES OR LIQUEFIED GASES | LPG, H2S, H2 ETC..
D (METAL) | FIRE THAT OCCUR IN COMPASTIBLE METALS | SODIUM,ZINC, POTTASIUM, MG ETC..

## Slide 20: METHODS OF HEAT TRANSFER
CONDUCTION
HEAT TRANSFER THROUGH A MEDIUM OF SOLID BODY.
CONVECTION
HEAT TRANSFER THROUGH UPWORD MOTION OF HEATED MATTERS.
RADIATION
HEAT TRANSFER THROUGH AIR HEAT WAVE.

## Slide 21: FIRE TRIANGLE

## Slide 22: STAGES OF FIRE
INCIPIENT STAGE
SMOULDRING STAGE
FLAME STAGE
HEAT STAGE

## Slide 23: STAGES OF FIRE
INCIPIENT STAGE
INVISIBLE PRODUCTS OF COMBUSTION GIVEN OFF, NO VISIBLE SMOKE, FLAAME OR HEAT.
SMOULDRING STAGE
COMBUSTION PRODUCTS NOW VISIBLE AS SMOKE. FLAME OR HEAT STILL NOT PRESENT.
FLAME STAGE
ACTUAL FIRE NOW EXITS
HEAT STAGE
UNCONTROLLED HEAT AND IT IS RAPIDLY EXPANDING IN SPACE

## Slide 24: EXTINGUISHING METHODS

## Slide 25: EXTINGUISHING METHODS
STARVATION
LIMITATION OR REMOVAL OF FUEL FROM THE SCENE OF FIRE IS KNOWN AS STARVATION
SMOTHERING
LIMITATION OR REMOVAL OF OXYGEN FROM THE SCENE OF FIRE IS KNOWN AS SMOTHERING
COOLING
LIMITATION OR REMOVAL OF HEAT FROM THE SCENE OF FIRE IS KNOWN AS COOLING

## Slide 26: EXTINGUISHING METHODS
STARVATION …… TO REMOVAL OF FUEL
SMOTHERING ...... TO REMOVEL OF OXYGEN
COOLING ….. TO REMOVAL OF HEAT

## Slide 27: EXTINGUISHING MEDIA
WATER
FOAM
DCP ( DRY CHEMICAL POWDER )
CO2
SAND

## Slide 29: HOW TO USE FIRE EXTINGUISHER
IT IS EASY TO REMEMBER HOW TO USE A FIRE EXTINGUISHER IF U CAN REMEMBER A SHOT FORM PASS WHICH STANDS FOR PULL, AIM, SQUEEZE & SWEEP

## Slide 31: CLASSIFICATION OF FIRE EXTINGUISHER

## Slide 32: PETROLEUM CLASSIFICATION
CLASS A ( LIQUIDS ) | FLASH BELOW 23*C | PETROL,LPG, ACETYLENE
CLASS B ( LIQUIDS ) | FLASH POINT BETWEEN 23*C & 65*C | KEROSENE
CLASS C ( LIQUIDS ) | FLASH POINT BETWEEN 65*C & 93*C | DIESEL OILS, FURNACE OIL
EXCLUDED PETROLEUM | FLASH POINT ABOVE 93 | 

## Slide 33: TYPES OF FIRE EXTINGUISHER
WATER

## Slide 34: TYPES OF FIRE EXTINGUISHER
FOAM

## Slide 35: TYPES OF FIRE EXTINGUISHER
D - DRY
C - CHEMICAL
P - POWDER

## Slide 36: FIRE EXTINGUISHEN ANATOMY

## Slide 37: FIRE EXTINGUISHEN ANATOMY
CO2 TYPE

## Slide 38: COLOUR OF EXTINGUISHER
WATER - RED
FOAM - CREAM
POWDER - BLUE
CARBON DIOXIDE - BLACK

## Slide 39: TYPES OF EXTINGUISHERS
GAS CARTRIDGE.
THE PRESSURE IS PRODUCED BY MEANS OF COMPRESSED OR LIQUEFIED GAS RELEASED FROM A GAS CARTRIDGE FITTED IN TO THE EXTINGUISHER.
STORED PRESSURE
THE EXPELLANT GAS IS STORED WITH THE EXTINGUISHING MEDIUM IN THE BODY OF THE EXTINGUISHER, WHICH IS THE PERMANENTIY PRESSURIZED.

## Slide 40: ADVANTAGES OF DCP
HARMLESS TO SKIN
NON-CONDUCTOR OF ELECTRICITY
GOOD FOR BLAST FIRE
BETTER THAN CO2 ON LIQUID FIRE
NON TOXIC AND NON CORRSOIVE

## Slide 41: DISADVANTAGES OF DCP
DCP CANNOT BE USED ON METAL FIRE LIKE SODIUM, MAGNESIUM ETC….
DCP CANNOT BE USED TO PRODUCE INERT ATMOSPHERE TO PREVENT GAS/VAPOUR

## Slide 42: FIRE EXTINGUISHER CHECKLIST
SI.NO | LOCATI-ON | TYPE | PRESSER GUAGE | SAFETY PIN | DUE DATE | OUTER CYLINDER | HOSE NOZZLE | RE-MARK
1 | GLOBAL MVPA | ABC |  |  | 10/17 |  |  | 
2 | GLOBAL MVPA | CO2 |  |  | 10/17 |  |  | 

## Slide 43: DEFINITIONS
ACCIDENTS
AN ACCIDENT IS UN DESIGNED AND UN PLANED EVENT THAT RESULT IN PERSONAL INJURY OR PROPERTY DAMAGE OR ENVIRONMENTAL POLLUTION.
INJURY
INJURY CAN BE DEFINED AS HARMFUL CONDITION SUSTAINED BY THE BODY RESULT OF AN ACCIDENT.
HAZARD
A SITUATION WITH THE POTENTIAL TO CAUSE HARM IN HAZARD

## Slide 44: DEFINITIONS
RISK
IT IS THE PROBABILITY OF THE REALIZATION OF THE POTENTIAL FOR LOSS
NEARMISS
AN UNPLANED AND UNDESIGHNED EVENT THAT HAD THE POTENTIAL TO LEAD TO INJURY DAMAGE OR LOSS.
TOOL BOX TALK
TOOL BOX TALK IS A PRE-JOB MEETING IN WHICH THE SUPERVISOR,SAFETY OFFICER CONCERNED WILL EXPLAIN TO THE WORKERS ABOUT THE JOB AND THE HAZARD.

## Slide 45: DEFINITIONS
WHO IS A COMPETENT PERSON ???
IS ONE WHO IS PROPERLY TRAINED AND AUTHORIZED TO PERFORM A SPECIFIC WORK IN A SAFE MANNER.

## Slide 46: STANDARED SAFETY SIGNAGE
MANDATORY- BLUE & WHITE

## Slide 47: STANDARED SAFETY SIGNAGE
PROHIBITION – RED & BLACK

## Slide 48: STANDARED SAFETY SIGNAGE
WARNING- YELLOW & BLACK

## Slide 49: STANDARED SAFETY SIGNAGE
SAFE CONDITION- GREEN & WHITE

## Slide 50: STANDARED SAFETY SIGNAGE
FIRE EQUIPMENTS

## Slide 51: FIRE DETECTORS
SMOKE DETECTOR

## Slide 52: FIRE DETECTORS
HEAT DETECTORS

## Slide 53: FIRE FIGHTING EQUIPMENTS
FIRE BLANKETS
HOSE REELS
FIRE FIGHTING HOSE
FIRE MONITOR
FIRE HYDRENT
SPRINKLER SYSTEM

## Slide 54: FIRE FIGHTING EQUIPMENTS
FIRE BLANKETS

## Slide 55: FIRE FIGHTING EQUIPMENTS
HOSE REELS

## Slide 56: FIRE FIGHTING EQUIPMENTS
FIRE FIGHTING HOSE

## Slide 57: FIRE FIGHTING EQUIPMENTS
FIRE MONITOR

## Slide 58: FIRE FIGHTING EQUIPMENTS
FIRE HYDRENT

## Slide 59: FIRE FIGHTING EQUIPMENTS
SPRINKLER SYSTEM

## Slide 60: COMMON CAUSES OF FIRE
SPARK FROM ELECTICITY
SMOKING
HOT WORK
NAKED FLAME
HOT SURFACE
SPARK FROM VEHICLES
LIGHTINING
STATIC ELECRTICITY

## Slide 61: CONSEQUENCE OF FIRE
PEOPLE KILLED AND INJURED
DAMAGE TO BUILDING
ENVIRONMENT DAMAGE

## Slide 62: DEFINITIONS
FLASH POINT
THE LOWEST TEMPERATURE AT WHICH THE COMBASTIBLE MATERIAL GIVE SUFFICENT VAPOUR TO START AN IGNITION.
FIRE POINT
THE LOWEST TEMPRATURE AT WHICH THE COMBASTIBLE MATERIAL GIVE SUFFIIENT VAPOUR TO CONTINEUS THE COMBUSTION.
IGNITION TEMPREATURE
THE LOWEST TEMPERATURE AT WHICH IT WILL SPONTANEOUSLY IGNITE IN A NORMAL WITH OUT AN EXTERNAL SOURCE OF IGNITION.

## Slide 63: DEFINITIONS
LEL- LOWER EXPLOSIVE LIMIT
THE LOWEST CONCENTRATION AT WHICH A FUEL MIXTURE WILL BURN.
UEL- UPPER EXPLOSIVE LIMIT
THE HIGHEST CONCENTRATION AT WHICH A FUEL MIXTURE WILL BURN.

## Slide 64: P- PERSONAL P- PROTECTIVE E- EQUIPMENT GLOBAL SAFETY STUDIES

## Slide 65: PPES

## Slide 66: PERSONAL PROTECTIVE EQUIPMENT
PERSONAL PROTECTIVE EQUIPMENT A VARIETY OF DEVICE,TO PROTECTE EMPLOYEES FROM INJURY.

## Slide 67: TYPES OF PPES
RESPIRATORY PROTECTIVE EQUIPMENTS
Eg; SCBA, AIR RESPIRATORS ETC..
NON- RESPIRATORY PROTECTIVE EQUIPMENTS
Eg; HARD HAT, GLOVES, GOGGLES, SAFETY SHOES ETC..

## Slide 68: NON-RESPIRATORY PROTECTIVE EQUIPMENTS
COMMON PPES
HEAD PROTECTION
EYE & FACE PROTECTION
HAND PROTECTION
FOOT PROTECTION

## Slide 69: HEAD PROTECTION
PREVENTION OF HEAD INJURES IS AN IMPORTANT FACTOR IN EVERY PROGRAM, HEAD INJURY ARE CAUSED BY FALLING, FLYING OBJECT OR BY JUMBING THE HEAD AGAINST A FIXED OBJECT..

## Slide 70: HEAD PROTECTION
HEAD INJURIES

## Slide 71: EYE & FACE PROTECTION
SUTABLE EYE PROTECTOR MUST BE PROVIDE, WHEN THERE IS A POTENTIAL FOR FACE FROM FLYING PURTICLE, LIQUIDS, CHEMICALS, CHEMICAL GAS, VAPOURS, POTTENTIALLY INJURIOUS LIGHT RADIATION OR COMBINATION OF THESE.

## Slide 72: TYPES OF EYE & FACE PROTECTION
SAFETY GLASSES
SAFETY GOGGLES
FACE SHIELDS
WELDING GOGGLES
LASER SAFETY GLASS

## Slide 73: EYE & FACE PROTECTION

## Slide 74: FOOT PROTECTION
FOR PROTECTION FEET AND LEGS FROM FALLING OBJECTS, SHARP OBJECTS, HOT SURFACE AND WET SURFACE.
SAFETY SHOES SHOULD BE STURDY AND HAVE RESISTANT TOE
SOME SHOE METAL INSOLE PROTECTE AGAINST PUNCTURE WOUNDS

## Slide 75: FOOT PROTECTION

## Slide 76: HAND PROTECTION
WHEN MUST HAND PROTECTION BE PROVIDE BURNS, ABRASION, CUTS, PUNCTURES, BRUISE, CHEMICAL EXPOSURE..

## Slide 77: HAND PROTECTION

## Slide 78: TYPES OF GLOVES
LEATHER GLOVES
COTTEN GLOVES
CHEMICAL PROTECTION GLOVES
INSULATED RUBBER GLOVES
WELDING GLOVES

## Slide 79: EAR PROTECTION
HEARING PROTECTION SHALL BE MADE AVAILABLE AND SHALL BE WORN BY ALL EMPLOYEES EXPLOSSED TO AN 8 HOUR OF 85 DB OR GREATER
EAR MUFF
EAR PLUG

## Slide 80: HEARING PROTECTORS
EAR PLUGS - PREFERRED ( 20-30 DB )
EAR MUFFS – 2ND CHOICE ( 15-30 DB )
DOUBLE HEARING PROTECTORES ( PLUG & MUFF )-
( 30-40 DB ) USED FOR LEVELS OVER 115 DB

## Slide 81: NOICE LEVELS
MEASURED IN DECIBELES ( DB )
* WHISPER - 10-20 DB
* SPEECH - 60 DB
* NOISY OFFICE - 80 DB
* PASSING TRUCK - 100 DB
* JET ENGINE – 150 DB
OSHA LIMIT – 85 DB

## Slide 82: PERMISSIBLE EXPOSURE LIMIT – PEL
PERMISSIBLE NOISE EXPOSURE
DURTION PER DAY ( HOURS ) | SOUND LEVEL ( DB )
8 HOURS | 90 DB
4 HOURS | 95 DB
2 HOURS | 100 DB
1 HOURS | 105 DB
½ HOURS | 110 DB
¼ HOURS | 115 DB

## Slide 83: RESPIRATORY PROTECTIVE EQUIPMENTS
RESPIRATORY PROTECTIVE EQUIPMENTS ARE LIFE SAVING EQUIPMENTS

## Slide 84: TYPES OF PROTECTIVE DEVICES
AIR PURIFYING DEVICES
AIR SUPPLYING DEVICES
COMBINATION OF AIR PURIFYING AND AIR SUPPLYING DEVICES

## Slide 85: AIR PURIFYING DEVICES
THE AIR PURIFYING DEVICES CLEANS THE CONTAMINATED ATMOSPHERE.
THE VARIOUS TYPES OF AIR PURIFYING DEVICE
* MECHANICAL FILTTERS CARTRIDGE
* CHEMICAL CARTRIDGE
* GAS MASC
* POWDERED AIR PURIFYING DEVICES

## Slide 86: AIR PURIFYING DEVICES

## Slide 87: AIR SUPPLYING DEVICES
AIR SUPPLYING DEVICES ARE THE CLASS OF RESPIRATORS THAT PROVIDE A RESPIRABLE ATMOSPHERE TO THE WEARER, INDIPENDENT OF THE AMBIENT AIR.
TYPES OF AIR SUPPLYING DEVICES
SELF CONTAINED BREATHING APPARATUS ( SCBA )
COMPRESSED AIR BREATHING APPARUTUS ( CABA )
EMERGENCY ESCAPING BREATHING APPARATUS

## Slide 88: BRATHING APPARUTUS ANATOMY

## Slide 89: SAFETY INSPECTION
DEFINITION ;
IT IS TO INVOLVE IDENTIFICATION OF OBVIOUS VISIBLE HAZARDS WITH THE OBJECTIVE OF ELIMINATING OR CONTROLE THE HAZARD THAT HAVE BEEN IDENTIFIED.
DURING A SITE SAFETY INSPECTION
HOUSE KEEPING
SAFETY SIGHN BOARD
WELFARE FACILITY
FENSING & SECURITY
STORES & STORAGE
FIRE EXTINGUISHER

## Slide 90
FIRE PROCEDURES
FIRST AID FACILITY
PPES
BARRICADING
SCAFFOLDING & WORKING PLATFORM
LADDER
CRANES & LIFTING EQUIPMENTS
EXCAVATION
CONFINED SPACE
ELECTRICITY
OVER HEAD & UNDER GROUND SERVICES
ELECTRICAL EQUIPMENT & HAND TOOL
WELDING EQUIPMENTS
SUBSTANCES HAZARDOUS TO HEALTH
OTHER HAZARDS

## Slide 91: HOUSE KEEPING
GLOBAL SAFETY STUDIES

## Slide 92: HOUSE KEEPING
DEFINITION
A PLACE FOR EVERY THING AND EVERY THING IN ITS PROPER PLACE.
GOOD HOUSE KEEPING IN THE KEY TO SAFETY.
HOUSE KEEPING IS EVERY ONE’S RESPONSIBILITY.

## Slide 93: HOUSE KEEPING
BENEFITS OF HOUSE KEEPING
GOOD HOUSE KEEPING PREVENTING ACCIDENTS AND INJURIES.
GOOD HOUSE KEEPING SAVE SAPCE,TIME AND MATERIALS.
WHEN A WORK PLACE IS CLEAN WORKERS FEEL BETTER, THINK BEETER, AND DO BETTER.
GOOD IMPRESSION WITH VISITORS
FIRE HAZARD ELIMINATION
MORE EFFITIVE USE OF SPACE

## Slide 94: HOUSE KEEPING
ACCIDENTS OF POOR HOUSE KEEPING
TRIPPING OVER LOOSE OBJECTS ON FLOORS,STAIRS AND PLATFORMS
BEING HIT BY FALLING OBJECTS
SLIPPING ON GREASY, WET OR DIRTY SURFACE
WASTE CONTAINER OVER FLOWING
TOOLS LEFT ON MACHINES

## Slide 95: HOUSE KEEPING
INJURIES FROM SLIPS, TRIPS, AND FALLS.
BROKEN BONES
BACK OR SPINE INJURY
STAINS/ SPRAINS
DEATH

## Slide 96: HOUSE KEEPING
GOOD HOUSE KEEPING
GOOD HOUSE KEEPING PREVENTING ACCIDENTS AND INJURIES.
ALL MATERIAL SHOULD BE PROPERLY STORED
KEEP BOLTS, NUTS, ETC… IN A TRAY/ BUCKET
PIPES, SCAFFOLD MATERISLS,ETC… ARE POTENTIAL TRIP HAZARD. DON’T STORE IN WALKWAY
DON’T STORE MATERIALS ON WORKING PLATFORM AND NEAR ACCESS LADDER/STAIR
DON’T ROUTE CABLES & HOSES THROUGH STAIRCASE / LADDER POSING POTENTIAL TRIP HAZARD
DON’T DRAIN STICKY MATERIAL/OIL ON FLOOR POSING SLIP HAZARD AND FALL HAZARD

## Slide 97: HOUSE KEEPING
DON’T USE FIRE WATER FOR CLEANING
DON’T BLOCK ACCESS TO FIRE AND EMERGENCY EQUIPMENTS
ALL MATERIAL SHOULD BE PROPERLY STORED

## Slide 98: HOUSE KEEPING
GOOD HOUSE KEEPING CHECKLIST
WALLS CLEANS
WINDOW CLEANS
PROPER LIGHT PROVIED
PLATFORM IN GOOD CONDITION
STAIRS CLEAN AND WET
FREE OIL, GREASE ETC…
SAFE AND FREE ACCESS TO WORK POSITION
EMPLOYEES FACILITIES
WASTE DISPOSAL
STORAGE
TOOLS AND EQUIPMENTS

## Slide 99: HOUSE KEEPING
WHAT IS YOUR FAVORITE PLACE TO WORK ?

## Slide 100: HOUSE KEEPING
BAD HOUSEKEEPING

## Slide 101: HOUSE KEEPING
GOOD HOUSE KEEPING

## Slide 102: HOUSE KEEPING
BAD HOUSE KEEPING

## Slide 103: ENVIRONMENT
GLOBAL SAFETU STUDIES

## Slide 104: ENVIRONMENT
DEFINITION
ENVIRONMENT MEANS THE SURROUNDING IN WHICH AS ORGANIZATION OPERATE INCLUDING AIR, WATER, LAND, NATURAL RESOURES, FLORA HUMAN AND THEIR INTER RELTIONSHIP.

## Slide 105: ENVIRONMENT
TYPES OF POLLUTION
AIR POLLUTION
WATER POLLUTION
SOIL POLLUTION

## Slide 106: ENVIRONMENT
EFFECTS OF POLLUTION
REDUCED LUNG FUNCTIONING
IRRITATION OF EYES, NOSE, AND MOUTH
ASTHMA ATTACK
RESPIRATORY DISEASE
REDUCE ENERGY LEVEL
HEAD ACHE
MENTAL DISORDER
CANCER
DEATH

## Slide 107: ENVIRONMENT
HOW TO SAVE ENVIRONMENT
DO NOT WASTE WATER
PREVENT POLLUTION ON THE GROUND, AIR, AND WATER BY AVIODING ANY CHEMICAL SPILLS
ENSURE ALL WASTE IS COLLECTED AND PLACED IN TO THE SPECFIC CONTAINERS
USE TOILET FACILITIES
DO NOT BURN WASTE
DO NOT KILL ANY WILD
REPORT ANY CHEMICAL SPILLS
SITE VEHICLE TO HAVE SPILL KITS
STORE CHEMICAL ONLY IN THE APPROVED STORAGE AREA WHERE SPILL KIT ARE AVAILABLE

## Slide 108: WASTE MANAGEMENT
WHAT IS WASTE MANAGEMENT ???..
WASTE MANAGEMENT MEANS SAFETY DISPOSING THE BY- PRODUCT OF A PROCESS OR A WORK TO THE ENVIRONMENT ( AFTER PROPER TREATMENT, IF NECESSARY) SO THAT NO THREAT FOR LIVINGS, PROPERTIES AND ENVIRONMENT EXISTS.

## Slide 109: WASTE DISPOSAL
CLASSIFICATION OF WASTE
HAZARDOUS WASTE
NON- HAZARDOUS WASTE

## Slide 110: WASTE DISPOSAL
HAZARDOUS WASTE
HIGHLY FLAMMABLE WASTE
CHEMICAL WASTE
TOXIC WASTE
CORROSIVE WASTE
ELECTRONIC WASTE
Etc….

## Slide 111: WASTE DISPOSAL
NON- HAZARDOUS WASTE
HOUSE WASTE
FOOD WASTE
PAPER
WOOD
COTTON
Etc…

## Slide 112: WASTE DISPOSAL
SEGREGATION
WASTE TYPES MUST BE SEGREGATED TO PREVENT THE MIXING AND CONTAMINATION OF ONE TYPE OF WASTE WITH ANOTHER. THIS USUALLY REQUIRES SEPARATE SECURE STORAGE FOR EACH TYPE WASTE AND THE CLEAR IDENTFICATION OF TYPES.

## Slide 113: MOVEMENTS OF PEOPLE
SLIP & TRIP
CAUSE- SLIP HAZARD
SMOOTH FLOOR SARFACE
WET
CONTAMINATION OIL
FROST AND ICE

## Slide 114: MOVEMENTS OF PEOPLE
CAUSE- TRIP HAZARD
UNEVEN OR LOOS FLOOR SURFACE
TRAILING CABLES
OBJECT AT FLOOR

## Slide 115: MOVEMENTS OF PEOPLE
CONTROL MESURESS
RISK ASSESSMENT
MANTANCE OF MECHINARY
SLIP RESISTANCE SURFACE , SPILLAGE CONTROL FOR SURFACE
GOOD HOUSE KEEPING
USE SINGH FOR PPE’S
LAY CABLES
DESIGNTED WALK WAYS

## Slide 116: MAIN CAUSES OF ACCIDENT
ACCIDENTS
AN ACCIDENT IS UN DESIGNED AND UN PLANED EVENT THAT RESULT IN PERSONAL INJURY OR PROPERTY DAMAGE OR ENVIRONMENTAL POLLUTION.
UNSAFE ACTION
UN SAFE CONDITION

## Slide 117: UNSAFE ACTION
DEFINITION
THESE ARE WHERE THE ACTION OF THE PEOPLE IN THE WORK PLACE DIRECTLY CAUSE OR CONTRIBUTE TO THE INCIDENT.
USE WRONG TOOLS
ARRANGING OR PLACEING OBJECT UNSAFELY
USING EQUIPMENTS UNSAFELY
OPERATING WITHOUT PERMITION

## Slide 118: UNSAFE ACTION
WORKING AT UNSAFE SPEED
USING DEFECTIVE EQUIPMENT & TOOLS
FAILURE TO USE OF PPE
IMPROPER LIGHTING
SMOKING
HORSE PLAY
NOT USING SAFETY DEVICES
NOT REPORTING SAFETY PROBLEMS
WORKING UNDER THE INFLUENCE OF ALCOHOL

## Slide 119: UNSAFE ACTION

## Slide 120: UNSAFE CONDITION
DEFINITION
THESE ARE WHERE THE PHYSICAL CONDITION AT THE WORK PLACE, OR THE METHODS OF WORK, DIRECTLY CAUSE OR CONTRIBUTE TO THE INCIDENT.
INADEQUATE GUARDING
DEFECTIVE TOOLS
INADEQUATE VENTILATION
EXCESSIVE NOICE

## Slide 121: UN SAFE CONDITION
NO PERSONAL PROTECTIVE EQUIPMENTS
WET AND SLIPPRY SURFACE
BAD HOUSEKEEPING
UNSAFE LIFTING
UNSAFE EQUIPMENTS
UNSAFE SYSTEM OF WORK
UNSAFE ENVIRONMENTL CONDITIONS

## Slide 122: UN SAFE CONDITION

## Slide 123: DOMINO THEORY
88% OF ACCIDENTS DUE TO UNSAFE ACTS.
10% OF ACCIDENTS DUE TO UNSAFE CONDITIONS.
2% ARE UNAVOIDABLE ACCIDENTS.

## Slide 124: ELECTRICAL SAFETY
GLOBAL SAFETY STUDIES

## Slide 125: ELECTRICAL SAFETY
ELECTRICITY
THE FLOW OF THE ELECTRON THROUGH A CONDUCTOR IN A CLOSED CERCUTE. THE FLOW THROUGH THE CONDUCTOR THRER MUST BE A POWER SOUECE.

## Slide 126: ELECTRICAL SAFETY
ELECTRICAL HAZARD
PRIMARY HAZARD
SECONDARY HAZARD

## Slide 127: PRIMARY HAZARD
ELECTRIC SHOCK
ELECTRIC BURN
ELECTRIC FIRE & EXPLOSION
ELECTRIC FLASH

## Slide 128: SECONDARY HAZARD
PERSON FALL FROM HEIGHT
LOSE OF INFORMATION
DROPPING OF TOOL AND OBJETS
UN EXPECTED MOVEMENTS OF MACHINERY
HEALTH HAZARD DUE TO RELEASE TOXIC GAS & PRODUCTION OF UV RAYS
ENVIRONMENTAL HAZARD

## Slide 129: ELECTRICAL SAFETY
EFFECTS OF ELECTRICAL SHOCK
DAMAGE TO NERVOUS SYSTEM
IRREGULAR HART BEAT
INTERNAL BURNS
STOP BREATHING
SKIN SURFACE BURN

## Slide 130: ELECTRICAL SAFETY
MAJOR CAUSE OF ELECTRICAL FIRE
OVERLOADING OF CERCUTE
OCTOPUS
IMPROPERLY RATE CERCUTE
POOR DAMAGE INSULATION
POOR CONNECTION
FLAMMABLE MATERIALS

## Slide 131: ELECTRICAL SAFETY
ELECTRICITY PROTECTION DEVICES
FUCES
EARTHING
ISOLATION
ELCB
MCB

## Slide 132: SAFETY ARRANGEMENTS
PROPER INSPECTION
PROPER DISTRIBUTION BOARD TO BE PROVIDED IN DIFFERENT AREA
ALL CAABLE JOINTS SHALL BE MADE WITH INDUSTRIAL PLUG
GENERATOR SHOULD BE GROUNDED
USE PROPER PPE
GENERATOR AREA TO BE CLEANED PROPERLY
NO FLAMMABLE NEAR DG
PROVIDE EXTINGUISHER, SIGN BOARD AND BARRICATION AROUND THE DG
NO CABLE ARE NOT TO BE LAID ON WET AREA

## Slide 133: ELECTRICAL SAFETY
INDUSTRIAL PLUG.

## Slide 134: ELECTRICAL SAFETY
EMERGENCY ACTION
DON’T TOUCH THE CASUALTY
CALL FOR HELP
ISOLATE FROM THE POWER SUPPLY
CALL FOR AMBULANCE
CHECK FOR BREATHING
TREAT BURNS
TREAT FOR PHYSICAL SHOCK
ENSHORE MEDICAL

## Slide 135: LOTO- (LOCK OUT TAG OUT)
GLOBAL SAFETY STUDIES

## Slide 136: LOTO
DEFINITION
LOCKOUT MEANS TO PHYSICALLY NETURALIZE ALL ENERGIES IN A PIECE OF EQUIPMENT BEFORE BEGINNING ANY MAINTENANCE OR REPAIR WORK. LOCK OUT GENERALLY INVOLVE , STOPPING ALL ENERGY FLOWS AND PROVIDE A TAG TO HELP CONTROL MECHANICAL AND ELECTRICAL ISOLATION PROCEDURES.

## Slide 137: LOTO- COLOUR CODE
ELECTRICAL DEPT; - RED
MECHANICAL DEPT; - YELLOW
INSTRUMENTATION DEPT - BLUE

## Slide 138: LOTO
DIFFERENT TYPES OF LOCKS

## Slide 139: ISOLATION
CUT OFF THE SPACE FROM ELECTRICAL SOURCES, ROTATING PARTS, HAZAEDOUS MATERIALS Etc….

## Slide 140: SCAFFOLDNG
GLOBAL SAFETY STUDIES

## Slide 141: SCAFFOLDNG
DEFINITION
SCAFFOLDING IS A TEMPORARY ELEVATED PLATFORM MADE FOR SAFELY WORKING AT HEIGHT.
INTRODUCTION
IT IS ESTIMATED THAT 2.3 MILLION CONSTRUCTION WORKERS DEAL WITH SCAFFOLDIG EATCH YEAR. MORE THAN 10000 WORKERS ARE INJURED AND 80 ARE KILLED IN SCAFFOLDING RELATED ACCIDENTS.

## Slide 142: TYPES OF SCAFFOLDS
FRAME SCAFFOLDING
TUBE AND CLAMP
MODULAR SYSTEM SCAFFOLDS
ROLLING SCAFFOLDING (MOBILE SCAFFOLDS)
SUSPENDED SCAFFOLDIND

## Slide 143: TYPES OF SCAFFOLDS
FRAME SCAFFOLDING

## Slide 144: TYPES OF SCAFFOLDS
TUBE AND CLAMP

## Slide 145: TYPES OF SCAFFOLDS
MODULAR SYSTEM SCAFFOLDS

## Slide 146: TYPES OF SCAFFOLDS
ROLLING SCAFFOLDING (MOBILE SCAFFOLDING)

## Slide 147: TYPES OF SCAFFOLDS
SUSPENDED SCAFFOLDIND

## Slide 148: TYPES OF SCAFFOLDING ( BASED ON WORKING LOAD)
LIGHT DUTY SCAFFOLD
MEDIUM DUTY SCAFFOLD
HEAVY DUTY SCAFFOLD
SPECIAL DUTY SCAFFOLD

## Slide 149: LIGHT DUTY SCAFFOLD
A SCAFFOLD DESIGNED AND CONSTRUCTED TO CARRY A WORKING LOAD NOT TO EXCEED 150kg/ M2

## Slide 150: MEDIUM DUTY SCAFFOLD
A SCAFFOLD DESIGNED AND CONSTRUCTION TO CARRY A WORKING LOAD NOT TO EXCEED 200 kg/M2

## Slide 151: HEAVY DUTY SCAFFOLD
A SCAFFOLD DESIGNED AND CONSTRUCTED TO CARRY A WORKING LOAD NOT TO EXCEED 250kg/M2

## Slide 152: SPECIAL DUTY SCAFFOLD
SCAFFOLD DESIGNED AND CONSTRUCTED TO CARRY SPECIFIC TYPE OF OBJECTS

## Slide 153: COMMON PARTS OF SCAFFOLD
SOLE BOARD/ SILLS
BASE PLATE
STANDARD/ POST
LEDGER
BRACE
TRANSOM
COUPLER
WORKING PLATFORM
GUARD RAILS
ACCESS LADDER

## Slide 154: COMMON PARTS OF SCAFFOLD
SOLE BOARD/SILLS
SILVER OAK WOODEN PLANK SUPPORRT BASE PLATE AT GROUND.

## Slide 155: COMMON PARTS OF SCAFFOLD
BASE PLATE
IT IS A MILD STEEL SQUARE-PLATE

## Slide 156: COMMON PARTS OF SCAFFOLD
STANDARD/POST
IT IS VERTICAL SCAFFOLD TUBE

## Slide 157: COMMON PARTS OF SCAFFOLD
LEDGER
IT IS HORIZONTAL SCAFFOLD TUBE

## Slide 158: COMMON PARTS OF SCAFFOLD
BRACE
A TUBE PLACED TO THE VERTICAL AND HORIZONTAL MEMBERS OF A SCAFFOLD AND FIXED TO THEM TO GIVE STABILITY.

## Slide 159: COMMON PARTS OF SCAFFOLD
TRANSOM
TUBES FIXED AT RIGHT ANGLE ACROSS THE LEDGERS, ADJACENT TO EATCH PAIR OF STANDAEDS TO SUPPORT THE SCAFFOLD BOARDS

## Slide 160: COMMON PARTS OF SCAFFOLD
COUPLER
A DEVICE FOR LOCKING TOGETHER COMPONENT PARTS OF TUBE AND COUPLER SCAFFOLD .

## Slide 161: COUPLER
TYPES OF COUPLERS

## Slide 162: COMMON PARTS OF SCAFFOLD
WORKING PLATFORM
AN ELEVATED WORK SURFACE COMPOSED OF ONE OR MORE PLATFORM UNITS.

## Slide 163: COMMON PARTS OF SCAFFOLD
GUARD RAILS
TOP RAIL
MID RAIL
TOE BOARD

## Slide 164: COMMON PARTS OF SCAFFOLD
GUARD RAILS- HEIGHT
TOP RAIL
MID RAIL
TOE BOARD
 | 70 CM |  | TOTAL- 110 CM
 | 40 CM |  | 
 | 15 CM |  | 

## Slide 165: LADDER
HAZARDS OF LADDERS
DON’T STAND LADDER ON DRUM, BOX OR OTHER UNSTABLE BASE
NEVER ATTEMPT TO REPAIR BROKEN LADDER
NEVER CARRY LOAD UP LADDER HOIST IT UP
WHEN USING THE METEL LADDER, , MAKE SURE THERE ARE NO ELECTRICAL HAZARD IN THE NEAR VICINITY
FALLING OFF THE LADDER

## Slide 166: LADDER
SAFE LADDER PLACING
LADDER SHOULD BE SET AN ANGLE OF ABOUT 75 OR ONE METER FOR EVERY FOUR METER RISE

## Slide 167: LADDER
LADDER-SAFETY
USE ONLY APPROVED LADDERS
INSPECT BEFORE USE
ONE PERSON ONLY
USE FALL ARREST IF > 6 FT WORKING FROM LADDER
EXTEND 3 FEET ABOVE ACCESS OR WORKING LEVEL
USE 4:1 LEAN RATIO
USE 3 POINT CONTACT

## Slide 168: LADDER
LADDER SAFETY

## Slide 169: LADDER
MONKEY LADDER

## Slide 170: HAZARDS- SCAFFOLDING
FALL FROM SCAFFOLD DURING ERACTION
FALL FROM WORKING PLATFORM
ELECTROCUTION- FROM OVERHEAD POWER LINES
FALLING OBJECT
SCAFFOLD COLLAPSE

## Slide 171: CAUSE OF SCAFFOLD COLLAPSE
OVER LOAD WORK PLATFORM
SOFT GROUND
NOT TIED IN PROPERLY
BRAZING INSAFFICENT
HIGH WIND
INCORRECT COUPLAR
SCAFFOLD ERECTED BY INCOMPETANT WORKERS
SCAFFOLD NOT INSPETED PRIOR TO USE

## Slide 172: SAFETY ARRAGEMENTS -SCAFFOLD
USE APPROPRIATE SCAFFOLD CONSTRUCTION METHOD
PROPER INSPECTION
TRAINED AND CERTIFIED WORKER
NOT EXCEED SAFE LOAD
ERECTION ON A LEVEL GROUND
10 FEET SAFE DISTANCE FROM POWER LINE
PROPER FALL PROTECTION SYSTEM

## Slide 173: SCAFFOLD FALL PROTECTION SYSTEM
GUARD RAIL
TOP RAIL
MID RAIL
TOE BOARD
TRAINING
BARRICATION
FULL BODY HARNESS
SAFETY NETS
SAFETY MONITORING
PFAS – PERSONAL FALL ARREST SYSTEM

## Slide 174: SCAFFOLD FALL PROTECTION SYSTEM
FULL BODY HARNESS

## Slide 175: FULL BODY HARNESS
PARTS OF HARNESS

## Slide 176: SCAFFOLD FALL PROTECTION SYSTEM
SAFETY NETS

## Slide 177: SCAFFOLD FALL PROTECTION SYSTEM
GUARD RAILS
TOP RAIL
MID RAIL
TOE BOARD

## Slide 178: SCAFFOLD INSPECTION CHECK LIST
CHECK FOR MISSING PLANKS ON PLATFORM
CHECK FOR MISSING GUARD RAIL SYSTEM
CHECK FOR PROPER ACCESS
CHECK FOR HOUSE KEEPING ON SCAFFOLD PLATFORM (LOOSE MATERIALS, WORKING WASTE ETC…)
CHECK FOR PROPER TYING OFF BUILDING

## Slide 179: SCAFF TAG SYSTEM
THREE TYPES OF SCAFF TAG
RED TAG – DON’T USE
GREEN TAG – OK TO USE
YELLOW TAG – CHECK WITH SUPERVISOR
IF THERE IS NO SCAFF TAG DON’T USE THE SCAFFOLD

## Slide 180: WORK AT HEIGHT
GLOBAL SAFETY STUDIES

## Slide 181: WORK AT HEIGHT
DEFINITION
WORK THERE IS A RISK OF FALL LIABLE TO CAUSE INJURY
ANY WORK ABOVE 1.8 METER FROM GROUND IS CAUSED WORK AT HEIGHT

## Slide 182: WORK AT HEIGHT
RESULT OF FALLING FROM HEIGHT
FATALITY
SPINAL INJURY
MULTIPLE BROKEN BONES

## Slide 183: WORK AT HEIGHT
HAZARDS OF WORK AT HEIGHT
VERTICAL HEIGHT
FALLING METERIALS
WEATHER
UN PROTECTED EDGS
SLOPPING ROOFS

## Slide 184: WORK AT HEIGHT
CONTROL MEASURE FOR WORKING AT HEIGHT
TRAINING
BARRICATION
FULL BODY HARNESS
SAFETY NETS
PFAS-PERSONAL FALL ARREST SYSTEM
GUARD RAILS

## Slide 185: MANUAL HANDLING
GLOBAL SAFETY STUDIES

## Slide 186: MANUAL HANDLING
DEFINITION
MANUAL HANDLING IS EVERY TASK WHICH INVOLVES PEOPLE MOVING HANDLING OR SHIFTING MATERIALS AND OBJECT

## Slide 187: MANUAL HANDLING
MANUAL HANDLING HAZARDS
TWISTING AND TURNING
HEAVY LOAD
DROPPING LOAD
SHARP EDGGES
HOT LOAD

## Slide 188: MANUAL HANDLING
MANUL HANDLING INJURIES
BACK INJURIES
MUSCULAR SPRAIN
CUTS AND ABRASION
FRACTURE
OPEN INJURIES
SWELLING
HERNIA

## Slide 189: MANUAL HANDLING TECHNIQUE
ASSESS THE LOAD
POSSITION OF FEET
BEND KNEES
LEG MUSCLE SUPPORT
BACK STRAIGHT
ARM CLOSED TO THE BODY
AVOID TWISTING

## Slide 190: EXCAVATION
GLOBAL SAFETY STUDIES

## Slide 191: EXCAVATION
DEFINITION
ANY MAN MADE CUT, TRENCH OR DEPRESSION IN AN EARTH SURFACE ,FORMED BY EARTH REMOVEL EITHER MANUALLY OR MECHANICALLY
WHAT IS TRENCH ???
TRENCH IS A NARROW EXCAVATION DEPTH IS GREATER THAN WIDTH

## Slide 192: EXCAVATION
EXCAVATION HAZARD
CAVE IN
WATER ACCUMULATION
OXYGEN DEFICIENCY
TOXIC AND FLAMMABLE GASES
FALLING OBJECTS
PEOPLE FALLING
SIDE WALL PROCTION COLLAPSE

## Slide 193: EXCAVATION
PREVENTIVE MEASURES
PROPER INSPECTION
PROVIED SIGN BOARD
BARRICADING
SUITABLE SIDE WALL PROCTION SYSTEM (SLOPING & BENCHING, SHORING, SHIELDING)
DE-WATERING SYSTEM
PROPER PPE
CONDUCT GAS TEST ( O2, CO, H2S, METHANE )
REMOVED SOIL , TWO FEET FROM THE SIDE
AROUND TRAFFIC, USE REFLECTIVE VETS
ACCESS LADDER

## Slide 194: EXCAVATION
EXCAVATION- SUITABLE SIDE WALL PROCTION SYSTEM
SLOPING & BENCHING SYSTEM
SHORING SYSTEM
SHIELDING SYSTEM

## Slide 195: EXCAVATION PROTECTION SYSTEM
SLOPING
A METHOD OF EXCAVATING IN WHICH THE SIDES OF AN EXCAVATION ARE LAID BACK TO A SAFE ANGLE TO PREVENT CAVE-IN

## Slide 196: EXCAVATION PROTECTION SYSTEM
BENCHING
A METHOD OF PROTECTING EMPLOYEES FROM CAVE-INS BY EXCAVATING THE SIDE S OF AN EXCAVATION TO FORM ONE OR A SERIES OF HORIZONTAL STEPS

## Slide 197: EXCAVATION PROTECTION SYSTEM
SHORRING
HYDRAULIC, TIMBER OR MECHANICAL SYSTEM THAT SUPPORT THE SIDES OF AN EXCAVATION , DESIGNED TO PREVENT CAVE-INS

## Slide 198: EXCAVATION PROTECTION SYSTEM
SHIELDING
A STRUCTURE THAT IS ABLE TO WITH STAND THE FORCES IMPOSED ON IT BY CAVE-INS, AND IN THE PROCESS, PROTECTS EMPLOYEES INSIDE THE STRUCTURE

## Slide 199: SITE CONDITION SHALL BE CHEKED BEFORE STARTING EXCAVATION
TRAFFIC
NEAREST STRUCTURES AND THEIR CONDITION
SOIL TEST
OVER HEAD AND UNDER GROUND UTILITIES ( TELEPHONE LINES,ELECTRONIC LINES,WATER LINES, OTHER PIPE LINES )

## Slide 200: EXCAVATION
PREVANCTION PEOPLE FALLING
BARRICATION AND TOE BOARD
GOOD LIGHT AND SIGN
CROSSING POINT
ACCESS LADDER
LADDER TO EXTANTS 1 MTR ABOVE EDGS OF EXCAVATION

## Slide 201: EXCAVATION
PROTECTION FROM VECHICLES
FENCE OR BARRICATION
HAND OR MECHANICAL SIGNAL
STOP LOGS
GRADE SOIL AWAY FROM EXCAVATION
GOOD LIGHTS

## Slide 202: EXCAVATION
GENARAL TIPS
ANY EXCAVATION OR TRENCH 4 FEET OR DEEPER SHALL BE CONSIDERED ON A CONFINED SPACE
IF THE WORK ARROUND THE TRAFFIC PEDESTRIAN SAFETY VERY IMPORTANT
A COMBITANT PERSON INSPECT EXCAVATION ON DAILY CHECK ADJACENT AREA FOR POSSIBLE CAVE-IN FAILAURE OF PROTECTIVE SYSTEM AND EQUIPMENT, HAZHADOUS ATMOSPHERE OR OTHER HAZARDOUS CONDITION.
IDENTYFY THE UNDER GROUND UTILITIES BY USING SITE MAP, UTILITIES DETECTORS, SIGN BOARD AND ROUTE MARKS

## Slide 203: TOOLS
GLOBAL SAFETY STUDIES

## Slide 204: TOOLS
TOOLS AND EQUIPMENTS ARE THREE TYPES
HAND TOOLS
POWER TOOLS
PNEUATICTOOLS

## Slide 205: TOOLS
COMMON HAZARDS
ELECTRIC SHOCK
FLASH BURNS
FALLING
HAND AND EYE INJURIES
CUT OR LOSSING A BODY PARTS
ERGONOMIC INJURIES

## Slide 206: TOOLS
BASIC TOOLS SAFETY RULES
MAINTAIN REGULARLY
USE RIGHT TOOLS FOR THE RIGHT JOB
INSPECT BEFORE USE
OPERATE ACCODING TO MANUFACTURE INSTRUCTION
USE THE RIGHT PPE’S
USE GUARDS

## Slide 207: TOOLS
HAND TOOLS
E.g...
HAMMERS
SCREWDRIVERS
CUTTERS
SPANNERS
HAND TOOLS HAZARDS
HAZARDS ARE USULLY CAUSED BY MISUSE AND IMPROPER MAINTENANCE

## Slide 208: TOOLS
HAND TOOLS-SAFETY TIPS
RIGHT TOOLS FOR THE RIGHT JOB
GOOD CONDITION
PROPER CARE AND MAINTANANCE
USE PROPER PPE
AVOID USE OF MUSHROOMED HAMMER AND CHIESSEL

## Slide 209: TOOLS
POWER TOOLS
TOOLS WHICH ARE RUN BY ELECTRICAL POWER SUPPLY IS KNOWN AS POWER TOOLS
ELECTRICAL DRILLS
ELECTRICAL GRINDER
JIG SAW
ELECTRICAL CUTTER
POWER TOOL HAZARDS
ELECTRICAL SHOCK
CUT OR LOSSING A BODY PARTS
BROKEN BONES
HIT

## Slide 210: TOOLS
POWER TOOLS – SAFETY TIPS
CABLE, PLUGS, ARE IN GOOD CONDITION
TOOLS USE WITH CORRECT POWER SUPPLY
MAKE SURE POWER SUPPLY TO BE PROPER EARTHED
TOOLS MUST BE SWITHCHED OFF BEFORE PLUG IN
USE PROPER PPE
KEEP TOOLS CLEAN AND DRY
DISCONNECT WHEN NOT IN USE
PROPER INSPECTION AND MAINTANANCE

## Slide 211: TOOLS
SAFETY TIPS- ANGLE GRINDER
RPM SPEED MUST BE GREATER THAN THE GRINDER SPEED
VALIDITY DATE; DO NOT USE IN CASE OF EXPIRY
ANGLE GRINDER & DISENGAGED DISC

## Slide 212: TOOLS
PNEUMATIC TOOLS
POWERED BY COMPRESSED AIR INCLUDES CHIPPER, DRILLS, SANDER.
PNEUMATIC TOOLS HAZARDS
MAIN HAZARD IS GETTING HIT BY TOOLS
NOICE IS AN OTHER HAZARD

## Slide 213: TOOLS
PNEUMATIC TOOLS – SAFETY TIPS
AUTHORISED OPERATOR
REGULARLY MAINTAINED AND SERVICED
PROTECTIVE GUARD IS CORRECLY FITTED BEFORE USE
PROPER PPE’S
TURN OF THE MAIN COMMPRESSED AIR SUPPLY LINE BEFORE DISCONNECTING
LEAKAGE OF AIR SHOULDN’T TOUCH BY HANDS
NEVER USE BODY FOR CLANING
KEEP THE TOOL IN HORIZONTAL POSSISSION WHEN CHANGING BITS OR POINTS

## Slide 214: CONFINED SPACE
GLOBAL SAFETY STUDIES

## Slide 215: CONFINED SPACE
DEFINITION
CONFINED SPACE AS ONE LIMITED OPENING FOR ENTRY OR EXIT, INSAFFICENT NATURNAL VENTILATION AND NOT DESIGNED FOR CONTINUOUS WORKER OCCUPENCY

## Slide 216: CONFINED SPACE
EXAMPLES OF CONFINED SPACES
STORAGE TANKS
MANHOLES
PIPE LINES
OIL PITS
WELLS
DUCTS
VESSELLS

## Slide 217: CONFINED SPACE
HAZARDS OF CONFINED SPACE
OXYGEN DEFICIENT ATMOSPHERE
OXYGEN ENRICHED ATMOSPHERE
FLAMMABLE ATMOSPHERE
TOXIC ATMOSPHERE
MECHANICAL AND ELECTRICAL HAZARDS
ENGULFMENT HAZARDS
WET SURFACE,FALLING OBJECTS
HIGH NOISE
POISONOUS CREATURE
HIGH TEMPERATURE

## Slide 218: CONFINED SPACE
POTENIAL HAZARDS IN CONFINED SPACE
OXYGEN DEFICIENCY
< 19.5% -23.5% OXYGEN CONCENTRATION
TOXIC MATERIALS
GASOLINE FUMES
CARBON MONOXIDE
HYDROGEN SULFIDE
WELDING FUMES
CORROSIVES

## Slide 219: CONFINED SPACE
COMBUSTIBLES MATERIALS
METHANE
HYDROGEN
ACETYLENE
PROPANE
ELECTRICITY OR MECHANICAL HAZARDS
MIXER
CRUSHER

## Slide 220: CONFINED SPACE
ATMOSPHERIC HAZARDS
OXYGEN DEFICIENCY
OXYGEN ENRICHMENT
COMBUSTTIBLE/ FLAMMABLE MATERIALS
TOXIC GASES

## Slide 221: CONFINED SPACE
OXYGEN DEFICIENT ATMOSPHERES
19.5% | SAFE ZONE, MINIMUM FOR SAFE ENTRY
15-19% | DECREASED ABILITY TO WORK.
12-14 % | RESPIRATION INCREASES. POOR JUDGMENT
10-12% | RESPIRATION INCREASES. LIPS BLUE
8-10% | MENTAL FAILURE, UNCONSCIOUSNESS, VOMITING, NAUSEA
6-8% | DIFFICULT BREATHING, DEATH IN MINUTES
4-6% | COMA IN 40 SECONDS, DEATH

## Slide 222: CONFINED SPACE
OXYGEN ENRICHED ATMOSPHERE
OXYGEN LEVEL ABOVE 23.5%
CAUSES FLAMMABLE AND COMBUSTIBLE MATERIALS TO BURN VIOLENTLY WHEN IGNITED
NEVER USE PURE OXYGEN TO VENTILATE
NEVER STORE OR PLACE COMPRESSED TANKS IN A CONFINED SPACE

## Slide 223: CONFINED SPACE
GENERAL HAZARDS
LIMITED ACCESS & EGRESS
LIMITED ILLUMINATION AND VENTILATION
SLIP AND FALL ON WET SURFACE
HIGH TEMPURATURE
POISONOUS CREATURES

## Slide 224: CONFINED SPACE
ENGULFMENT HAZARDS
POSSIBILITY OF ENGULFMENT BY FLOODING
WATER OR SEWAGE FLOW
LOOSE, GRANULAR MATERIALS

## Slide 225: CONFINED SPACE
MECHANICAL AND ELECTRICAL HAZARDS
UNEXPECTED MOVEMENTS OF MECHANICAL EQUIPMENTS
ELECTRIC SHOCK

## Slide 226: CONFINED SPACE SAFETY ARREGEMENTS
CHECK OXYGEN LEVEL, PERMISSIBLE IS 19.5% TO 23.5%
CHECK FOR FLAMMABLE GASES, BELOW 10% OF ITS LEL
CHECK THE CONCENTRATION OF TOXIC GASES AVAILABLE AND MEASURE WITH PPM
PROPER VENTILATION AND ILLUMINATION
ISOLATE THE SPACE BEFORE ENTERING
WORKER MUST BE TRAINED AND QULIFIED
PROVIED A SAFETY ATTENDANT OUT SIDE
USE SUITABLE PPE’S
USE EXTRA LOW VOLTAGE EQUIPMENTS (24 v)

## Slide 227: CONFINED SPACE SAFETY ARREGEMENTS
PERSONAL ENTRY/ EXIT LOG SHEET SHALL BE MAINTAINED
FOR COLUMNS, TANKS AND OTHER SLUDGE CONTAMINATED CONFINED SPACES, FIRST ENTRY SHALL BE WITH AIRLINE RESPIRATOR ONLY
ALL MAN WAYS SHALL BE BARRICADED AND NO ENTRY WITH OUT PERMIT SIGN SHALL BE POSTED

## Slide 228: CONFINED SPACE SAFETY ARREGEMENTS
MECHANICAL VENTILATION
BY USING FILTERED COMPRESSED AIR
BY USING A BLOWER FAN
BY USING AN EXHAUST FAN

## Slide 229: CONFINED SPACE
WHO IS ENTRANT
THE EMPLOYEE WHO WILL PHYSICALLY ENTER THE CONFINED SPACE TO PERFORM THE WORK.WHO MUST BE TRAINED AND EXPERIENCED PERSON.

## Slide 230: CONFINED SPACE
WHO IS HOLE WATCHER/ SAFETY ATTENDANT
THE ATTENDANT IS THE PERSON STAMP OUTSIDE THE CONFINED SPACE AND IS RESPONSIBLE FOR ASSISTING THE ENTRANT IN EXTING THE CONFINED SPACE AND CALLING FOR EMERGENCY ASSISTANCE WHILE REQUIRED

## Slide 231: HOLE WATCH- DUTIES & RESPONSIBILITY
CHECK OXYGEN LEVEL
CHECK FLAMMABLE GASES
CHECK TOXIC GASES
PERSONAL ENTRY/ EXIT LOG SHEET SHALL BE MAINTAINED
PERMIT AVAIABLE ON LOCATION AND CHECK VALIDITY
RESCUE PROCEDURE DISSCUSSED WITH WORKERS
AIR SUPPLY AVAIBLE ON LOCATION
PROPER VENTILATION AND ILLUMINATION
USE EXTRA LOW VOLTAGE EQUIPMENTS
ALL MAN WAYS SHALL BE BARRICADED AND NO ENTRY WITH OUT PERMIT SIGN SHALL BE POSTED
ALL RECOMMORED PPES ARE USED

## Slide 232: CONFINED SPACE
CONFINED SPACE- GENARAL TIPS
THERE SHOULD BE GOOD COMMUNICATION BETWEEN ENTRANT AND ATTENDANT
CONDUCT THE GAS TEST EVERY HOUR AND TEST ALL AREA OF CONFINED SPACE TOP, MIDDLE, AND BOTTOM OF THIS SPACE.
BECAUSE SOME GAS HEAVIR THAN AIR SOME GAS LIGHT THAN AIR .
COMMON CHANCE TOXIC GASES IN CONFINED SPACE ARE CO AND H2S

## Slide 233: H2S- HYDROGEN SULPHIDE
GLOBAL SAFETY STUDIES

## Slide 234: H2S- HYDROGEN SULPHIDE
DEFINITION
IT IS MAINLY FORMED BY CHEMICAL REACTION AND BIOLOGICAL DE COMBINATION.
H2S IS ONE OF THE DANGEROUS NATURAL GASES .
INDUSTRIAL SOURCES OF H2S.
GAS PROCESSING, OIL/ GAS PRODUCTION & DRILLING RIGS, HYDROCARBON REFINING, OIL STORAGE TANKS, SEWAGE TREATMENT PLANTS, ETC.

## Slide 235: H2S- HYDROGEN SULPHIDE
PROPERTIES OF H2S.
TOXICITY
COLORLESS
ODORLESS
HEAVIER THAN AIR
FLAMMABILITY
SOLUBILITY
CORROSIVITY
H2S IS DISPERSED BY THE WIND

## Slide 236: H2S- HYDROGEN SULPHIDE
EMERGENCY / FIRST AID MEASURE
INHALATION; REMOVE THE VICTIM TO FRESH AIR AREA, PROVIDE ARTIFICIAL RESPIRATION OR OXYGEN IF NEEDED.
EYES; IRRIGATE WITH PLENTY OF WATER FOR 15 MINS.
SKIN; REMOVE THE CONTAMINATED CLOTHING AND WASH THE AFFECTED AREA WITH PLENTY OF WATER AND SOAP.SEEK MEDICAL AID IMMEDIATELY

## Slide 237: SO2- SULFUR DIOXIDE
PROPERTIES OF SO2
HIGHLY TOXIC IF INHALED
COLORLESS
HEAVIER THAN H2S AND AIR
HIGHLY CORROSIVE
NON-FLAMMABLE

## Slide 238: H2S TOXICITY TABLE
H2S CONCENTRATION | EFFECT ON VICTIM
LESS THAN 1 PPM | DETECTABLE BY SMELL
10 PPM | POSSIBLE HEADACHE
ABOVE 30 PPM | EYE & RESPIRATORY IRRITATION
ABOVE 100 PPM | LOSS OF SENSE OF SMELL
ABOVE 500 PPM | DIZZINESS, NAUSEA, ABDOMINAL PAINS
700 TO 1000 PPM | RAPID UNCONSCIOUSNESS
ABOVE 1000 PPM | RAPID COLLAPSE AND DEATH

## Slide 239: TYPES OF GAS DETECTORS
PORTABLE MULTI-GAS DETECTORS.
AREA MULTI-GAS DETECTORS.
PERSONAL H2S GAS MONITOR.
FIXED GAS DETECTORS.

## Slide 240: GAS DETECTORS
PORTABLE MULTI-GAS DETECTORS.
THE PORTABLE GAS DETECTORS ARE FITTED WITH ELECTRO CHEMICAL SENSORS AND USED TO TEST OXYGEN, TOXIC, AND FLAMMABLE GAS LEVELS IN THE WORK TO COMPLY WITH THE PERMIT TO WORK. THE DETECTOR PRODUCES AN AUDIBLE ALARM, A FLASHING VISUAL ALARM AND VIBRATING ALARM ON GAS DETECTION AT TLV OR ABOVE.

## Slide 241: GAS DETECTORS
AREA MULTI-GAS DETECTORS.
USED AS A SINGLE UNIT OR LINKED TOGETHER FOR AREA PROTECTION . MONITORS FOR DANGEROUS LEVELS OF OXYGEN, METHANE, H2S, AND CORBON MONOXIDE.

## Slide 242: GAS DETECTORS
PERSONAL H2S GAS MONITOR.
PERSONAL H2S GAS MONITOR IS TWO YEAR , MAINTENANCE AND CALIBRATION FREE, DISPOSABLE SINGLE GAS MONITOR. THE GAS MONITOR PRODUCES A LOUD AUDIBLE ALARM, A VIBRATION,AND A BRIGHT FLASHING VISUAL ALARM ON H2S DETECTION AT 10 PPM OR ABOVE.
NOTE : PERSONAL H2S GAS MONITOR SHOULD NOT BE USED FOR GAS TESTING.

## Slide 243: GAS DETECTORS
FIXED GAS DETECTORS.
FIXED GAS DETECTORS ARE USED AS A H2S MONITORING DEVICE ON INSTALLATIONS. THIS CAN BE LINKED TO CONTROL ROOM BY WHICH, WE CAN IDENTIFY THE EXACT LOCATION OF DETECTION.

## Slide 244: FIRST-AID
GLOBAL SAFETY STUDIES

## Slide 245: FIRST-AID
IN THE EVENT OF AN ACCIDENT, YOU SHOULD ACT IN THE FOLLOWING WAY;
PREVENT MORE PEOPLE FROM BEING INJURED
CALL THE SUPERVISOR OR THE PERSON RESPONSIBLE FOR FIRST AID TREATMENT. CALL AMBULANCE IF NECESSARY
AID THE INJURED PERSON

## Slide 246: FIRST-AID
AIMS OF FIRST AID
PRESERVE LIFE
TO PREVENT CONDITION IS WORSEING
TO PROMOTE RECOVERY
CPR- CARDIAC PULMONARY RESUSCIATION

## Slide 247: WELFARE FACILITIES AT SITE
MANAGEMENT MUST BE PROVIDED PROPER WELFARE FACILITIES TO WORKERS
TOILETS
WASHING FACILITIES
DRINKING WATER
REST ROOM
PRAYER HALL
SMOKING AREA
FIRST AID FACILITIES
FACILITIES FOR INTAKE OF MEALS

## Slide 248: PERMIT TO WORK
GLOBAL SAFETY STUDIES

## Slide 249: PERMIT TO WORK
DEFINITION
A LEGAL DOCUMENT AND A FORMAL WRITTEN STATEMENT OF WORK TO BE DONE, SAFETY PRECAUTIONS TO BE TAKEN AND CONFIRMATION THAT ASSOCIATED RISK AND HAZARD HAVE BEEN IDENTIFIED
WORK PERMIT IS AN IMPORTANT ACCIDENT PREVENTION TOOL

## Slide 250: PERMIT TO WORK
WHAT IS WORK PERMIT SYSTEM ???
A WORK PERMIT IS A DOCUMENT WHICH SPECIFIES THE WORK TO BE DONE AND THE PRECAUTIONS TO BE TAKEN
WORK PERMIT FORM AN ESSENTIAL PART OF SAFE SYSTEM OF WORK FOR MANY MAINTENANCE ACTIVITIES

## Slide 251: PERMIT TO WORK
TYPES OF WORK PERMIT
HOT WORK PERMIT
COLD WORK PERMIT
CONFINED SPACE ENTRY PERMIT
ELECTRICAL WORK PERMIT
RADIOGRAPHY PERMIT
VEHICLE , MACHINERY PERMIT
ROAD CLOSE PERMIT
EXCAVATION PERMIT

## Slide 252: PERMIT TO WORK
PERMIT CHEKLIST
PERMIT NUMBER;
WORK REQUEST;
WORK DESCRIPTION
HAZDRDS/ DANGERS
PRECAUTIONS REQUIRED
ISOLATION DETAILS
PURGING SYSTEM
SITE PREPARATION
PROTECTIVE & SAFETY EQUIPMENT

## Slide 253: PERMIT TO WORK
ASSOCIATED PERMITS/ CERTIFICATES
GAS TEST- AUTHORISED GAS TESTER
SIGN FOR PERMIT CONTROLLER, PERFORMING AUTHORITY, WORK SITE SUPERVISOR
PERMIT CONTROLLER SHIFT CHANGE/TRANSFER ENDORSEMENT
AREA AUTHORITY ENDORSEMENT

## Slide 254: PERMIT TO WORK
SUPORTING DOCUMENTS PTW
WORK METHOD STATEMENTS
JOB SAFETY ANALTSIS
RISK ASSESSMENT
TRAINING REPORTS
THRID PARTY CERTIFICATE
PTW CHECKLIST
AREA DRAWING

## Slide 255: VEHICLE COLLISION
GLOBAL SAFETY STUDIES

## Slide 256: VEHICLE COLLISION
COLLISION CAN OCCUR BETWEEN THE VEHICLE
OTHER VEHICLE
PEDESTRIANS
FIXED OBJECT

## Slide 257: VEHICLE COLLISION
FACTORS THAT INCREASE THE RISK OF VEHICLE COLLISION
DRIVER ERROR (eg ,DRIVING TOO FAST)
INADEQUATE LIGHTING
REVERSING WITH OUT THE HELP OF A BANKSMAN
BAD WEATHER CONDITION
OBSTRUCTED VISIBILITY
POOR DESIGN OF PEDESTRIAN WALKWATS AND CROSSING POINT
LACK OF VEHICLE MAINTENANCE (eg ,BREAK FAILURE)

## Slide 258: FORK LIFT
GLOBAL SAFETY STUDIES

## Slide 259: FORK LIFT
FACTORS THAT MAY CAUSE A FORKLIFT TRUCK TO OVERTURN
DRIVING AROUND CORNERS TOO QUICKLY
UNEVEN LOADING OF THE FORK
DRIVING WITH THE LOAD ELEVATED , ESPECIALLY WHEN GOING AROUND CORNERS
UNEVEN TYRE PRESSURE
EXCESSIVE BREAKING
DRIVING ACROSS A SLOPE RATHER THAN STRAIGHT UP OR DOWN THE SLOPE
COLLISION , ESPECIALLY WITH KERBS

## Slide 260: FORK LIFT

## Slide 261: FORK LIFT
FORKLIFT SAFETY
USE SAFE SPEED
BE AWARE OF FORK POSITION
WATCH OUT THE BLIND SPORTS
SLOW DOWN AND SOUND HORN AT THE CORRNER
CERTIFIED FORKLIFT OPERATORS ONLY
INSPECT THE FORKLIFT BEFORE EATCH SHIFTS

## Slide 262: FORK LIFT
PRE- USE – CHECK – FORKLIFT
TYRE PRESSURE
PARKING BRAKES
STEERING
FUEL, OIL AND WATER SYSTEM FOR LEAKE
BATTERIES
LIFTING AND TILTING SYSTEM
AUDIBLE WARNING
LIGHTS
MIRRORS

## Slide 263: FORK LIFT
PARKING RULES FOR A FORKLIFT
APPLY THE HAND BREAK
LOWER THE FORK AND TIP THE FORWARD
REMOVE THE KEY
PARK IT ON LEVEL AREA
DO NOT OBSTRUCT TRAFFIC
DO NOT OBSTRUCT THE PEDESTRIANS WALKWAYS
DO NOT OBSTRUCT THE EMERGENCY ESCAPE ROUTS

## Slide 264: CRANE & LIFTING EQUIPMENTS
GLOBAL SAFETY STUDIES

## Slide 265: CRANE
CRANE IS A MECHANICAL DEVICE USED TO HANDLING MATERIALS , STRUCTURE LIFTING AND DISTRIBUTING THE LOAD
TYPES OF CRANES
MOBILE CRANE
HYDRAULIC CRANE
OVERHEAD CRANE
GANTRY CRANE
TOWER CRANE

## Slide 266: MOBILE CRANE

## Slide 267: HYDRAULIC CRANE

## Slide 268: OVERHEAD CRANE

## Slide 269: GANTRY CRANE

## Slide 270: TOWER CRANE

## Slide 271: CRANE & LIFTING
CRANE & LIFTING PTW
TRAFFIC PERMIT
METHOD STATEMENT
JOB SAFETY ANALYSIS
TRAINING REPORT
AREA DROWING
LIFTING PLAN
THIRD PARTY CERTIFICATES
EQUIPMENTS CERTIFICATES
OTHER CERTIFICATES

## Slide 272: CRANE
MAJOR CAUSES OF CRANE ACCIDENTS
CONTACT WITH POWER LINES
OVERTURNS
FALLS
MECHANICAL FAILURES

## Slide 273: CRANE
HOW DO ACCIDENTS OCCUR
INSTABILITY-UNSECURED LOAD, LOAD CAPACITY EXCEEDEDD, OR GROUND NOT LEVEL OR TOO SOFT
LACK OF COMMUNICATION-THE POINT OF THE OPERATION IS A DISTANCE FROM THE CRANE OPERATOR OR NOT IN FULL VIEW OF THE OPERATOR
LACK OF TRAINING
INADEQUATE MAINTENANCE OR INSPECTION

## Slide 274: CRANE & LIFTING PARTS

## Slide 275: CRANE & LIFTING
CRANE HAZARDS
IMPROPER LOAD RATING
EXCESSIVE SPEEDS
NO HAND SIGNALS
INADEQUATE INSPECTION AND MAINTENANCE
UNGUARED PARTS
UNGUARED SWING RADIOUS
WORKING TOO CLOSE TO POWER LINES
SHATTERED WINDOWS
NO STEPS/ GUARD RAILS WALKWAYS
NO BOOM ANGLE INDICATOR
NOT USING OUTRIGGERS

## Slide 276: CRANE & LIFTING
CRANE OPERATION- SAFETY ARRAGEMENT
PROPER INSPECTION
TRAINED OPERATOR WITH VALID LICENCE
VALID THIRD PARTY CERTIFICATE OF ALL LIFTING GEARS
PROPER BARRICADING AND SINGH BOARD
LOAD RATING CHART & OPERATING MANUVAL IN THE CABIN
NEVER EXCEED SAFE WORKING LOAD (SWL)
10 FEET DISTANCE FROM POWER LINE
EXPERICNCED RIGGERS TEAM

## Slide 277: CRANE & LIFTING
CRANE OPERATION- SAFETY ARRAGEMENT
DAILY INSPECTION OF LIFTING GEARS
PROPER COMMUMICATION & SIGNALS
USE TAG LINE , IF NECESSARY

## Slide 278: CRANE & LIFTING
WHO IS RIGGER SUPERVISOR
RIGGER SUPERVISOR IS A PERSON WHO HAS OVERALL CONTROL OF LIFTING OPERATION , MUST BE TRAINED AND EXPERIENCED

## Slide 279: CRANE & LIFTING
RIGGING EQUIPMENTS & SLINGS
WIRE ROPE
FIBER ROPE
SYNTHETIC WEB SLING
WIRE ROPE WEB SLING
CHAIN BLOCK
D- SHACKLES
I- BOLTS
LIVER HOIST ( CHAIN PULLER)

## Slide 280: CRANE & LIFTING
RIGGING EQUIPMENTS & SLINGS

## Slide 281: CRANE & LIFTING
COLOUR CODE – WEB SLINGS
1 TON | VIOLET
2 TON | GREEN
3 TON | YELLOW
4 TON | GRAY
6 TON | BROWN
10 TON | RED

## Slide 282: CRANE & LIFTING
CRANE OPERATION- SAFETY TIPS
NEVER WALK OR STAND UNDER ANY SUPENDED LOAD
ALL SIGNAL MUST BE RECEIVED FROM AUTHORIZED SIGNAL MEN
BAD WEATHER – STOP LIFTING ( HIGH WIND AND RAIN)
THIRD PARTY CERTIFICATION OFF ALL LIFTING EQUIPMENTS

## Slide 283: MATERIAL STORAGES
GLOBAL SAFETY STUDIES

## Slide 284: MATERIAL STORAGES
PREVENTION OF FALLING OF MATERIALS FROM MATERIAL STACK
STACKING OF MATERIALS
STACK MATERIALS SEPARATELY
MAXIMUM HEIGHT FOR STACKING
STACK VERTICALLY
USE PALLETS
ALLOW SUFFICENT SPACE AROUND STACKS
PROTECT STACK FROM BEING STRUCK BY VEHICLES

## Slide 285: MATERIAL STORAGES
SAFE STORAGE MATERIALS
SEPARATE STORAGE AREA FOR MATERIALS
AREA SHOULD BE KEPT CLEAN AND TIDY
WARRNING SIGN
FLAMMABLE LIQUDS AND GASES SHOULD BE STORED SEPARATELY
STORE MADE OF FIRE RESISTANT MATERIALS
KEEP IGNITION SOURRCE AWAY
FIRE FIGHTING EQUIPMENTS
REGULAR INSPECTION

## Slide 286: MATERIAL STORAGES
SAFE STACKING AND STORAGE OF FLAMMABLE MATERIALS
LIQUIDS, SOLIDS, GASES IN SPARATE STORAGE
STORAGE OXYGEN SPEPARATE FROM OTHER GASES
FIRE – RESISTANCE INTERNAL STORAGE
WARRING SINGH / SAFETY SIGNGH
NO HOT WORK IN NEAR STORAGE AREA
FIRE FIGHTING EQUIPMENTS PROVIDED
INSPECT REGULARLY
CORRECTLY RATED ELECTRICAL EQUIPMENTS

## Slide 287: MATERIAL STORAGES
SAFETY RULES- OXYGEN CYLINDER
OXYGEN CYLINDER SHOULD NOT BE KEPT NEAR COMMBUSTIABLE MATERIALS
OXYGEN CYLINDER SHOULD NOT BE HANDLE WITH GRASSY HANDS OR GLOVES
OXYGEN CYLINDER THEIR FITTING SHOULD NOT BE TESTED WITH OIL BASED SOAP SOLUTION
THE TOP COVER OF THE CYLINDER SHOULD BE KEPT IN POSITION AND SCREWED SAFETY WHEN NOT IN USE.
CYLINDER SHOULD NOT BE USED AS ROLLERS FOR MOVING MATERIALS

## Slide 288: HOT & COLD ENVIRONMENT
GLOBAL SAFETY STUDIES

## Slide 289: HOT & COLD ENVIRONMENT
EFFCET OF EXPOSURE TO EXTREME HEAT
HYPERTHERMIA - DEHYDRATION
MUSCLE CRAMP
HEAT STRESS - INCREASES DISCOMFORTS, HEADACHE
HEAT STROKE
SKIN BURN, SKIN CANCER

## Slide 290: HOT & COLD ENVIRONMENT
EXPOSURE OF COLD ENVIRONMENT
FROST BITE
SLIP HAZARD
FREEZE BURN INJURY

## Slide 291: HOT & COLD ENVIRONMENT
CONTROL MEASURES
HOT ENVIRONMENT
VENTILATION
INSULATION
COOL REFUGES
DRINKING WATER
APPROPRITE CLOTHING
JOB ROTATION

## Slide 292: HOT & COLD ENVIRONMENT
COLD ENVIRONMENT
CLOSE VENTILATION
WARM REFUGES
HOT FOOD AND DRINKS
JOB ROTATION
REMOVE ICE
INSULATING JACKETS

## Slide 293: ACCIDENT REPORTING
GLOBAL SAFETY STUDIES

## Slide 294: ACCIDENT REPORTING
ACCIDENT
AN ACCIDENT IS UN DESIGNED AND UN PLANED EVENT THAT RESULT IN PERSONAL INJURY OR PROPERTY DAMAGE OR ENVIRONMENTAL POLLUTION.

## Slide 295: ACCIDENT REPORTING
BENEFITS OF ACCIDENT REPORTING & INVESTIGATION
PREVENTING RECURRENCE
IDENTIFYING OUT- DATED PROCEDURES
IMPROVED WORK ENVIRONMENT
INCREASED PROCEDURES
RAISES SAFETY AWARENESS
INCREASED REPUTATION & MORALE
BENEFITS ARE TO ALL

## Slide 296: ACCIDENT REPORTING
WHAT SHOULD BE REPORTING
ALL INJURIES OR JOB RELATED ILLNESSES
NEAR-MISS INCIDENTS
EQUIPMENT DAMAGE
POTENTIALLY UNSAFE CONDITION
POTENTIALLY UNSAFE ACTION

## Slide 297: ACCIDENT REPORTING
ACCIDENT REPORT
DEPARTMENT -
SUPERVISOR NAME -
DATE OF ACCIDENT -
TIME OF ACCIDENT -
NAME OF INJURED PERSON -
WORKS NUMBER -
RESON FOR ACCIDENT -
WITNESSES -
CORRECTIVE ACTION -
RECOMMENDATIONS -

## Slide 298: JOB SAFETY ANALYSIS- (JSA)
GLOBAL SAFETY STUDIES

## Slide 299: JOB SAFETY ANALYSIS- (JSA)
DEFINITION
JSA IS A CARFUL STUDY FOR EACH STEP IN A JOB, IDENTIFING THE SAFETY AND HEALTH HAZARD EACH STEP INDIVIDULLY AND IDENTIFYING APPROPRATE CONTROLS TO ELEMINATE OR REDUCE EACH HAZARD

## Slide 300: JOB SAFETY ANALYSIS (JSA)
JSA STEPS
STEP- 1 - SELECT THE JOB TO BE DONE
STEP- 2 - BREAK THE JOB DOWN IN TI STEEP
STEP- 3 - HAZARDS IDENTIFICATION
STEP- 4 - CONTROL MEASURE

## Slide 301: JOB SAFETY ANALYSIS (JSA)
SELECT JOB | JOB STEP | HAZARD IDE- NTIFICATION | CONTROL MEASURE
PROJECTOR INSTALLATION | MATERIALS ARRAGEMENT TO THE SITE | LACK AWARNESS, SUPERVISON, TRIP & FALL | AWARENESS FOR MANUVAL HANDLING, GOOD HOUSE KEEPING, QUALIFIED SUPERVISOR
 | WORKING PLAT FORM CONSTR- UCTION & DIS- MANTLING | UNSKILLED LABORS, IMPROPER SUPERVISION | TRAINED & COMPETENT WORKER & SUPERVISOR, FOLLOW SCAFF-SAFETY PROCEDURE. AWARENESS TALK,

## Slide 302: JOB SAFETY ANALYSIS (JSA)
SELECT JOB | JOB STEP | HAZARD IDE- NTIFICATION | CONTROL MEASURE
 | PROJECTOR MOUNTING | STANDARD POWER TOOLS, LACK OF TRAINING, SUPERVISION | ALL POWER TOOL MUST BE GOOD CONDITION AND INSPECTED, FOLLOW PROPER INSTALATION METHOD

## Slide 303: JOB SAFETY ANALYSIS (JSA)
IT IS HELP TO IDENTIFY HAZARD AND PREVENT ACCIDENT
IT IS HELP TO ESTABLISH SAFE WORK METHOD, WORKING CONDITION
IT IS HELPS TO INSPECTION THE PLANT

## Slide 304: EMERGENCY PLANNING
EMERGENCY PLANNING CAN DEFINED AS A CONTROL MEASURE . IT CAN CONTROL THE ACCIDENTS SAFE GUARD PEOPLE AND PROVIED INFORMATION TO MEDIA.

## Slide 305: ASSEMBLY POINT
A DESIGNTED PLACE WHERE PEOPLE HAVE BEEN TOLD TO WAIT AFTER EVACUATING IN THE EVENT OF A FIRE OR OTHER EMERGENCY.

## Slide 306: EVACUATION PROCEDURE
SOUND OF ALARM
GET OUT THE BUILDING
STAY OUT OF THE BUILDING ( ASSEMBLY POINT)

## Slide 307: EVACUATION PROCEDURE
SOUND OF ALARM

## Slide 308: EVACUATION PROCEDURE
GET OUT THE BUILDING
NO USE OF LIFT
TWO OR MORE SEPARATE ROUTES MAY BE REQUIRED
STAIRS, CORRIDORS,AND DOOR ARE FIRE RESISTANT PROTECTION
DOORS OPEN DIRECTION OF TRAVEL
TRAVEL DISTANCE SHOULD BE SHORT
ADQUATE WIDTH
CLEARLY SIGNED
EMERGENCY LIGHTS
NO OBSTRUCTION

## Slide 309: EVACUATION PROCEDURE
STAY OUT OF THE BUILDING ( ASSEMBLY POINT)
SAFE DISTANCE FROM THE BUILDING
SAFE LOCATION
FURTHER ESCAPE POSSIBLE IF NEEDED
CLEARLY SIGNED

## Slide 310: MOCK DRILL
A MOCK DRILL IS A METHOD OF PRACTISING HOW A BUILDING WOULD BE EVACUATED IN THE EVENT OF A FIRE OR OTHER EMERGENCY

## Slide 311: ERGONOMICS
GLOBAL SAFETY STUDIES

## Slide 312: ERGONOMICS
DEFINITION
THE STUDY OF THE RELATIONSHIP BETWEEN THE WORKER, THE WORK, THE EQUIPMENT AND THE ENVIRONMENT.
THE TOOLS, EQUIPMENT OR MACHINERY THAT THEY ARE USING
THE WORK PLACE ENVIRONMENT ( Eg; SUITABILITY OF LIGHTING )

## Slide 313: ERGONOMICS
ASBESTOS DUST -ASBESTOSIS
VIBRATION -VIBRATION WHITE FINGER
SITTING FOR TOO LONG -BACK PAIN, NECK ACHE
LACK OF LIGHTING -HEADACHES,EYE STRAIN

## Slide 314: ERGONOMICS
IT PROFESSIONAL HEALTH & SAFETY
AN ERGONOMICALLY STUDY ABOUT COMPUTER USERS HEALTH PROBLEMS & SAFE OPERATION.
POTENTIAL HEALTH EFFECTS
BODY FATIGUE
UPPER LIMP PAINS AND DISCOMFORT
EYE STRAIN
HEADACHES
NECK ACHE
STRESS & FATIGUE

## Slide 315: ERGONOMICS
GOOD ERGONOMIC WORK STATION

## Slide 316: HOT WORK
GLOBAL SAFETY SYUDIES

## Slide 317: HOT WORK
DEFINITION
ANY WORK WHICH INVOLVE THE USE OF NAKED FLAME OR A SOURCE OF IGNITION OR SPARK GENARATING POTENCTIONAL, CAPABLE OF IGNITING A COMBUSTIBLE OR EXPLOSIVE MATERIALS IS CLASSIFIED AS HOTWORK

## Slide 318: SOURCE OF IGNITION
SPARK FROM ELECTICITY
SMOKING
NAKED FLAME
HOT SURFACE
SPARK FROM VEHICLES
LIGHTINING
STATIC ELECRTICITY

## Slide 319: HOT WORK
SAFETY ARRANGEMENTS
BOOTH PREPARATION
PROPER INSPECTION
CHECK THE HOT WORK PERMIT
TEST FOR OXYGEN LEVEL
TEST FOR LEL
TRAINED/ EXPERIENCED WORKER
PROPER SUPERVISION
KEEP COMBUSTIBLE AWAY
FIRE WATCH AND SUITABLE EXTINGUISHER
PROPER VENTILATION & ILLUMINATION
PROPER HOUSEKEEPING

## Slide 320: HOT WORK
INSPECT TOOLS AND EQUIPMENTS
ELECTRIC DEVICE- INSULATED AND EARTHED
GAS CYLINDER- UP RIGHT POSITION
GAS REGULATER AND PRESSURE GAUGE- GOOD CONDITION
FLASH BACK ARRESTOR
FIRST-AID KIT
BARRICADE AND SIGN BOARD

## Slide 321: FIRE WATCH
DEFINITION
A PERSON WHO IS ASSIGNED AS LOOKOUT IN HOT WORK JOB
Eg; WELDING
CUTTING
GRINDING

## Slide 322: HOT WORK
FIRE WATCH- DUTIES AND RESPONSIBILITY
MAKE SURE REMOVE FROM FLAMMABLE MATERIALS AND EXPLOSIVE MATERIALS THAT WORK PLACE
CHECK THE HOT WORK PERMIT
CHECK TO THAT AREA CLEAN
CHECK AREA FOR NO HOT WORK SIGN AND OTHER POSTED DANGER MARKING
KNOW EXACT LOCATION OF ACETYLENE AND OXYGEN SHUT OFF VALVE
TEST FOR OXYGEN LEVEL AND LEL LEVEL
MAINTANE FIRE HOSE, FIRE EXTINGUISHER,AND FIRE BLANKET

## Slide 323: HOT WORK
CHECK TO SEE THAT THERE IS ADEQUATE VENTILATION
KNOW THE LOCATION FIRE ALARM AND EMERGENCY TELEPHONE
BARRICADE AREA & SIGN BOARD
LOCATE EMERGENCY EXITS AND MAKE SURE THEY ARE KEEPT FREE OF OBSTRUCTION

## Slide 324: COLD WORK
DEFINITION
ANY WORK THAT DOES NOT INVOLVING A SOURCE OF IGNITION OR NAKED FLAME OR DOES NOT HAVE SPARK GENARATING POTENCTIONALS IS CLASSIFIED AS COLD WORK
Eg; SCAFFOLDING , HOUSEKEEPING, MANUAL HANDLING Etc….

## Slide 325: HOLE WATCH/ SAFETY ATTENDANT
THE ATTENDANT IS THE PERSON STAMP OUTSIDE THE CONFINED SPACE AND IS RESPONSIBLE FOR ASSISTING THE ENTRANT IN EXTING THE CONFINED SPACE AND CALLING FOR EMERGENCY ASSISTANCE WHILE REQUIRED

## Slide 326: DEMOLITION
GLOBAL SAFETY STUDIES

## Slide 327: DEMOLITION
DEFINITION
DEMOLITION MEANS TOTAL DISTRACTION AND DISMANTILING OF THE STRUCTURE.

## Slide 328: DEMOLITION
HAZARDS
PREMATURE COLLAPSE
WORK AT HEIGHT
LIVE OVER HEADS
ASBESTOS
DUST
EXPLOSSIVE
MANUVAL HANDLING
BIOLOGICAL HAZARD
SHARPS EDGS

## Slide 329: DEMOLITION
CONTROL MEASURES
STRUCRURAL SURVEYS
HAZAEDOUS MATERIALS REMOVED
CHANGE OF METHOD TO REDUCE PEOPLE
SECURITY FOR THE SITE
DAMPING DOWN TO MINIMISE DUST ( WITH WATER )
DISCONNECTION OF SERVICES

## Slide 330: MATERIAL SAFETY DATA SHEETS ( MSDS)
GLOBAL SAFETY STIUDES

## Slide 331: MSDS
WHAT IS AN MSDS ???
MATERIAL SAFETY DATA SHEET
DEVELOPED BY CHEMICAL MANUFATURERS AND IMPORTERS
AN MSDS MUST BE ON HAND FOR EACH HAZARDOUS CHEMICAL USED BY THE COMPANY

## Slide 332: MSDS
WHERE ARE YOUR MSDS
MSDS….
MUST BE READILY ACCESSIBLE TO EMPLOYEES DURING THEIR WORK SHIFT
ARE TYPICALLY KEPT IN A CENTRALIZED LOCATION
MUST BE UPDATED AS NEW INFORMATION BECOMES AVAILABLE

## Slide 333: MSDS
WHAT INFORMATION IS ON AN MSDS
CHEMICAL NAME
MANUFACTURE INFO ( NAME,ADDRESS, TELEPHONE)
LIST OF INGREDIENTS
HAZARD IDENTIFICATION
FIRST-AID MEASURE
FIRE- FIGHTING MEASURE
HANDLING AND STORAGE
CONTROLS AND PERSONAL PROTECTION
TRANSPORT INFORMATION

## Slide 334: RISK ASSESSMENT
GLOBAL SAFETY STUDIES

## Slide 335: RISK ASSESSMENT
RISK
IT IS THE PROBABILITY OF THE REALIZATION OF THE POTENTIAL FOR LOSS.
RISK ASSESSMENT
A FORMALISED PROCESS OF IDENTIFYING HAZARDS ASSESSING THE RISK THAT THEY GENERATE AND THEN EITHER ELIMINATING OR CONTROLLING THE RISK.

## Slide 336: RISK ASSESSMENT
RISK ASSESSMENT CAN BE DESCRIBED AS A FIVE- STEP PROCESS
IDENTIFY THE HAZARDS
IDENTIFY THE PEOPLE WHO MIGHT BE HARMED AND HOW
EVALUATE THE RISK AND DECIDE ON PRECAUTION
RECORD THE SIGNIFICANT FINDING AND IMPLEMENT THEM
REVIEW AND UPDATE AS NECESSSARY

## Slide 337: RISK ASSESSMENT
HAZARD IDENTIFICATION METHODS
INSPECTION
TASK ANALYSIS
LEGISLATION
MANUFACTURERS INFORMATION
INCIDENT DATA

## Slide 338: RISK ASSESSMENT
IDENTIFYING THE PEOPLE AT RISK
WORKER/ OPERATOR
MAINTENANCE STAFF
CLEANERS
CONTRACTORS
VISITORS
MEMBERS OF THE PUBLIC

## Slide 339: RISK ASSESSMENT
EVALUATE THE RISK AND DECIDE ON PRECAUTION
RISK= LIKELIHOOD SEVERITY
BY SIMPLY ASSIGNING A SCORE TO EACH WORD IT IS POSSIBLE TO CALCULATE A RISK RATING FOR A PARTICULAR HAZARD.
Eg…
LIKELIHOOD | SEVERITY
1=EXTREMELY UNLIKELY | 1=VERY MINOR INJURY
2=UNLIKELY | 2=FIRST AID INJURY
3=POSSIBLE | 3=LOST TIME INJURY
4=LIKELY | 4=HOSPITAL TREATMENT
5=VERY PROBABLE | 5=DISABLING INJURY

## Slide 340: RISK ASSESSMENT

## Slide 341: RISK ASSESSMENT
A CONSTRUCTION COMPANY USE THE FOLLOWING TIME SCALES IN RELATION TO THE RISK RATING SYSTEM.
RISK RATING | ACTION AND TIME SCALE
15 AND ABOVE | UNACCEPTABLE WORK MAY NOTSTART,ADDITIONAL CONTROL MUST BE INTRODUCED TO REDUCE BELOW 9.
9 TO 14 | TOLERABLE ADDITIONAL CONTROL MUST BE INTRODUCED AS SOON AS POSSIBLE AND NO LATER THAN 24 HOURS AFTER ASSESSMENT.
5 TO 8 | TOLERABLE MUST BE REDUCE TO BELOW 5 WITHIN ONE WEEK
4 OR BELOW | ACCEPTABLE IF SIMPLE ACTION CAN REDUCE FURTHER THEN MUST BE DONE WITHIN ONE WEEK.

## Slide 342: RISK ASSESSMENT
RECORDING SIGNIFICANT FINDINGS
THE SIGNIFICANT FINDINGS OF A RISK ASSESSMENT SHOULD BE RECORDED TO PROVIDE A STATEMENT OF THE HAZARD IN THE WORKPLACE, THE EXTENT OF THE RISKS THAT THEY PRESENT, AND THE ACTION TAKEN TO CONTROL THOSE RISKS.

## Slide 343: GOAL TO IMPROVE SAFETY
GOOD HOUSE KEEPING AT WORK SITE
INCREASE GOOD CITIZENS BY 100 % PPE’S
JOB WISE RISK IDENTFICATION
REPORTING NEAR MISS, UNSAFE ACTS/CONDITION
100% PLANT SPECIFIC TRAINING AND MEDICAL
LEARNING FROM INCIDENT/ACCIDENT
MOBILE PHONE RESTRICTION IN THE PLANT AREA
ZERO ACCIDENT/INCIDENT
DAILY AND WEEKLY TOOLBOX TALK
WEEKLY/MONTHLY HAND TOOL INSPECTION
MONTHLY INSPECTION OF PPE’S

## Slide 344: GOAL TO IMPROVE SAFETY
MONTHLY INTERNAL SAFETY AUDIT
NEW EMPLOYEES JOB RELATED TRAINING AND SAFETY INDUCTION TRAINING
BEHAVIOR CHANGE IN TECHNICIANS TOWARDS WORK SAFETY
IMPLEMENTATION OF AWARDING SYSTEM

## Slide 345: SAFETY DOCUMENTS
PROJECT PLAN FILE
SAFETY INDUCTION DETAILS
TOOL BOX TALK REPORT
DAILY OBSERVATION REPORT
OBSERVATION CLOSEOUT REPORT
SAFETY INSPECTION REPORT
PROJECT JSA/ RA
ACCIDENT/ INCIDENT REPORT
NEAR MISS REPORT
FIRST AID REPORT
THIRED PARTY CERTIFICATE
CALIBRATION CERTIFICATE

## Slide 346: SAFETY DOCUMENTS
INSURANCE CERTIFICATE
MEDICAL CERTIFICATE
WEEKLY HSE REPORT
WORK METHOD STATEMENT
CLOSE OUT PTW
MSDS FILE
MOCK DRILL REPORT
WASTE DISPOSAL RECORD

## Slide 347: SAFETY PROMOTIONAL ACTIVITIES
TRAINING PROGRAM ( SAFETY INDUCTION, TBT Etc…)
SAFETY NOTICE BOARD
SAFETY BANNERS
SAFETY STICKER
SAFETY SIGN
SAFETY SLOGANS
SAFETY AWARDS
MOCK DRILLS

## Slide 348: SAFETY PROMOTIONAL ACTIVITIES
SAFETY SLOGANS

## Slide 349: HELICOPTER ANATOMY

## Slide 350: ABBREVIATIONS.
SAFETY- STAY ALERT FOR EACH TASK YOU DO
FIRE - FIND INFORM, RESTRICT,EXTINGUISH
HSE - HEALTH SAFETY ENVIRONMENT
OSHA - OCCUPATIONAL SAFETY AND HEALTH ADMINISTRATION
IOSH -INSTITUTION OF OCCUPATIONAL SAFETY AND HEALTH
NEBOSH- NATIONAL EXAMINATION BOARD IN OCCUPATIONAL SAFETY AND HEALTH
NFPA - NATIONAL FIRE PROTECTION ASSOCIATION
NSC - NATIONAL SAFETY COUNCIL
NBC -NATIONAL BUILDING CODE
PTW - PERMIT TO WORK

## Slide 351: ABBREVIATIONS.
TBT - TOOL BOX TALK
RA - RISK ASSESSMENT
TRA - TASK RISK ASSESSMENT
HIRA - HAZARD IDENTIFICATION RISK ASSESSMENT
JSA - JOB SAFETY ANALYSIS
JHA - JOB HAZARD ANALYSIS
NM - NEAR MISS
FAK - FIRST AID KIT
FAC - FIRST AID CASE
LTI - LOST TIME INJURY
PPM - PART PER MILLION
HID - HAZARD IDENTIFICATION

## Slide 352: ABBREVIATIONS.
DCP - DRY CHEMICAL POWDER
FMB - FOAM MAKING BRANCH
AFFF - AQUEOUS FILM FOAMING FOAM
LOTO - LOCKOUT AND TAGOUT
CPR - CARDEO PURLMINORY RESUSCITATION
PASS - PULL AIM SQUEECE SWEEP
STOP - SAFETY TRAINING OBSERVATION PROGRAMME
HAZOP- HAZARD OPERABILITY STUDY
NRV - NON RETURN VALVE
MSDS - MATERIAL SAFETY DATA SHEET

## Slide 353: ABBREVIATIONS.
SCBA - SELE CONTAINED BREATHING APPARATUS
CABA - COMPRESSED AIR BREATHING APPARATUS
LEL - LOWER EXPLOSIVE LIMIT
UEL - UPPER EXPLOSIVE LIMIT
PEL - PERMISSIBLE EXPLOSIVE LIMIT
STEL - SHORT TERM EXPLOSIVE LIMIT
ILDH - IMMEDIATE LIFE DEATH HAZARD
SWL - SAFE WORKING LOAD
PFAS - PERSONNEL FALL ARRESTER SYSTEM
ELCB - EARTH LEAKAGE CIRCUIT BREAKER
GLCT - GUARD LEAKAGE CIRCUIT INTERPTER
MCB - MINIATURE CIRCUIT BREAKER